## Slide 1
Computer Organization & Design
Hardware Software Interface
Xiaohong Jiang

## Slide 2: Chapter 2 Instructions: Language of the Computer

## Slide 3
The process of compiling and assembling
Assembly Instruction
a symbolic representation of machine instructions

## Slide 4: 2.1 Introduction
Language of the machine
  Instructions
  Instruction set
Computer Designer goals
  Find a language that makes it easy to build hardware and compiler.
  Maximize performance
  Minimize cost & energy
  Clarity of its application
  Simplicity: reduce design time
Our chosen instruction set: MIPS
  Similar to other ones developed since the 1984's
  Used by NEC, Nintendo, Silicon Graphics, Sony

## Slide 5: MIPS & ARM & RISC V
Category | MIPS | ARM | RISC V
Arithmetic | ADD $r1, $r2, $r3 | ADD r1, r2, r3 | ADD x5, x6, x7
 | SUB $r1, $r2, $r3 | SUB r1, r2, r3 | SUB x5, x6, x7
Data Transfer | LW $r1, 100($r2) | LDR r1, [r2, #100] | LW x5, 100(x6)
 | SW $r1, 100($r2) | SDR r1, [r2, #100] | SW x5, 100(x6)
 | LH $r1, 100($r2) | LDRH r1, [r2, #100] | LH x5, 100(x6)
 | SH $r1, 100($r2) | SDRH r1, [r2, #100] | SH x5, 100(x6)
Logical | AND $r1, $r2, $r3 | AND r1, r2, r3 | AND x5, x6, x7
 | SLL $r1, $r2, 10 | LSL r1, r2, #10 | SLL x5, x6, x7
Conditional branch | SLT $r1, $r2, $r3 | CMP r1, r2 | BLT x5, x6, x7
 | Beq $r1, $r2, Lable | BEQ Lable | BEQ x5, x6, 100
 | Bne $r1, $r2, Lable |  | BNE x5, x6, 100
Unconditional branch | J Lable | B Label | 
 | JAL Lable | BL Label | JAL x1, 100
 | JR $ra | Mov PC LR | JALR x1, 100(x5)

## Slide 6: Von Neumann’ Computer
Today’s computers are built on 2 key principles: (Stored-program concept)
  ①Instruction are represented as numbers.
  ②Programs can be stored in memory to be read or written just like numbers.
http://10.214.47.99:8080/mips/

## Slide 7: Four Design Principles
1. Simplicity favors regularity
2. Smaller is faster
3. Good design demands good compromises
4. Make the common case fast

## Slide 8
If you are asked to design the instruction set of computer, what will be the main elements ?

## Slide 9: Contents of Chapter 2
2.1 Introduction
2.2 Operations of the Computer Hardware
2.3 Operands of the Computer Hardware
2.4 Signed and Unsigned Numbers
2.5 Representing Instructions in the Computer
2.6 Logical Operations
2.7 Instructions for Making Decisions
2.8 Supporting Procedures in Computer Hardware
2.9 Communicating with People
2.10 MIPS Addressing for 32-bit Immediates and Addresses

## Slide 10
2.11 Parallelism and Instructions: Synchronization
2.12 Translating and Starting a Program
2.13 A C Sort Example to Put It All Together
2.14 Arrays Versus Pointers
2.15 Compiling C and Interpreting Java
2.16 Real Stuff: ARMv7 Instructions
2.17 Real Stuff: x86 Instructions
2.18 Real Stuff: ARMv8 Instructions
2.19 Fallacies and Pitfalls
2.20 Concluding Remarks
2.21 Historical Perspective and Further Reading

## Slide 11: 2.2 Operations of the Computer Hardware
Every computer must be able to perform arithmetic
  Only one operation per instruction
  Exactly three variables add a,b,c a←b+c
Design Principle 1
  Simplicity favors regularity
Ex 2.1 Compiling two simple C statements
  C code:
  a = b + c;
  d = a – e;
  MIPS code:
  add a, b, c
  sub d, a, e
Notes: Simplicity favors regularity：简单性来自规则性

## Slide 12
Instruction Set
Important design principles when defining the
instruction set architecture (ISA):
  keep the hardware simple – the chip must only
  implement basic primitives and run fast
  keep the instructions regular – simplifies the
  decoding/scheduling of instructions

## Slide 13: Assembly code
Opcode: the field that denotes the operation and format of an instruction.
  add, sub, lw, sw, beq, …
Operand
  register, memory, immediate, …
Assembly instruction
  Add x, y, z
    x = y + z
  Sub a, b, c
    a = b - c
opcode
0～3 opeands
The natural number of operands for an operation like addition is 3.
Requiring every instruction to have exactly 3 operands, no more and no less.

## Slide 14
A Basic MIPS Instruction
C code: a = b + c ;
Assembly code: (human-friendly machine instructions, a symbolic representation of machine instructions)
add a, b, c # a is the sum of b and c
Machine code: (hardware-friendly machine instructions)
00000010001100100100000000100000
The translation from C to MIPS assembly language instructions is performed by the compiler.
The translation from MIPS to machine code is performed by the assembler.

## Slide 15: Ex 2.2 Compiling a complex C statement
C code:
  f = ( g + h ) – ( i + j );
MIPS code:
  add t0, g, h # temporary variable t0 contains g + h
  add t1, i, j # temporary variable t1 contains i + j
  sub f, t0, t1 # f gets t0 – t1
Category | Instruction | Example | Meaning | Comments
Arithmetic | add | add a,b,c | a←b+c | Always three operand
 | subtract | sub a,b,c | a←b-c | Always three operand
  MPIS assembly language

## Slide 16: 2.3 Operands of the Computer Hardware
Register Operands
  Arithmetic instructions operands must be registers
  Difference between the variables of a programming
    Registers is limited number of special locations
      32 registers in MIPS
      32 bits for each register in MIPS
Design Principle 2: Smaller is faster
Limited instruction field
MIPS convention for registers
  $s0, $s1, … for registers corresponding to variables in C
  $t0, $t1, … for temporary registers for compiler
Why 32 Regs?

## Slide 17
Registers
The MIPS ISA has 32 registers (ARM has 16 registers) –
Each register is 32-bit wide (modern 64-bit architectures
have 64-bit wide registers)
A 32-bit entity (4 bytes) is referred to as a word
To make the code more readable, registers are
partitioned as $s0-$s7 (C/Java variables), $t0-$t9
(temporary variables)…
Where to put the Array or Structure ?
Memory！

## Slide 18: MIPS Register Conventions

## Slide 19: Memory operands
Save complex data structures
    Arrays and structures
Data transfer instructions
  Load: from memory to register; load word ( lw )
  Store: from register to memory; store word( sw )
Memory addresses and contents at those locations
…
Registers
12
8
4
0

## Slide 20
Memory Operands
Values must be fetched from memory before (add and sub)
instructions can operate on them
Load word
lw $t0, memory-address
Store word
sw $t0, memory-address
Register
Memory
Register
Memory
How is memory-address determined?

## Slide 21
Memory Operands
In C, each “variable” is a location in memory
In hardware, each memory access is expensive – if
variable a is accessed repeatedly, it helps to bring the
variable into an on-chip scratchpad and operate on the
scratchpad (registers)
To simplify the instructions, we require that each ALU instruction (add, sub) only operate on registers
Note: the number of operands (variables) in a C program is very large; the number of operands in assembly is fixed… there can be only 16-32 scratchpad registers

## Slide 22
Memory Address
The compiler organizes data in memory… it knows the
location of every variable (saved in a table)… it can fill
in the appropriate memory-address for load-store
instructions(L/S)
int a, b, c, d[10]
Memory
…
Base address
d[0], d[1], d[2], … (4 bytes for each int)

## Slide 23: Ex2.4 Compiling with an operand is in memory
C code
  g = h + A[8] ; // A is an array of 100 words ( Assume: g ---- $s1 h ---- $s2 base address of A ---- $s3 )
MIPS code:
  lw $t0, 8($s3) # temporary reg $t0 gets A[8]
  add $s1, $s2, $ t0 # g = h + A[8]
  Offset: the constant in a data transfer instruction →8($s3)
  Base register: the register added to form the address
Byte addressing →8($s3)中的offset must be 4*8
Alignment restriction
  Addresses of words are multiples of 4 in MIPS

## Slide 24
Data Transfer instruction
The format of a load instruction:
destination register
source address
lw $t0, 8($t3) ; $t0  MEM[ $t3 + 8 ]
any register
a constant that is added to the register in brackets
Could you explain “Sw $t0, 8($t3)” ?

## Slide 25: Byte addressing vs. word addressing
3 | 100
2 | 10
1 | 101
0 | 1
12 | 100
8 | 10
4 | 101
0 | 1
Word address： xxxxxxxx..xxx00
Double Word address：xxxxxxxx..xx000

## Slide 26: Memory Alignment: each variable stores at a word address
struct {
int a;
char b;
char c[2];
char d[3]
float e;
}
错误
因为内存一次只能读出4字节内存中的一行
这样布局，e变量不能一次读出
e |  |  | 
Unused | D[2] | D[1] | D[0]
Unused | Unused | C[1] | C[0]
Unused | Unused | Unused | b
a |  |  | 
Unused | e |  | 
e | D[2] | D[1] | D[0]

## Slide 27: Ex2.5 Compiling using load and store
  C code:
  A[12] = h + A[8] ; // A is an array of 100 words
  ( Assume: h ---- $s2 base address of A ---- $s3 )
MIPS code:
  lw $t0 , 32($s3) # temporary reg $t0 gets A[8]
  add $t0, $s2, $t0 # temporary reg $t0 gets h + A[8]
  sw $t0, 48($s3) # stores h + A[8] back into A[12]
A12 |  |  | 
A11 |  |  | 
A10 |  |  | 
A9 |  |  | 
A8 |  |  | 
A7 |  |  | 
A6 |  |  | 
A5 |  |  | 
A4 |  |  | 
A3 |  |  | 
A2 |  |  | 
A1 |  |  | 
A0 |  |  | 
Base Addr

## Slide 28: Ex2.6 Compiling using a variable array index
  C code:
  g = h + A[i] ; // A is an array of 100 words
  (Assume: g, h, i -- $s1, $s2, $s4 ；
  base address of A-- $s3 )
A12 |  |  | 
A11 |  |  | 
A10 |  |  | 
A9 |  |  | 
A8 |  |  | 
A7 |  |  | 
A6 |  |  | 
A5 |  |  | 
A4 |  |  | 
A3 |  |  | 
A2 |  |  | 
A1 |  |  | 
A0 |  |  | 
Base Addr
i
MIPS code:
  add $t1, $s4, $s4 # temp reg $t1 = 2 * i
  add $t1, $t1, $t1 # temp reg $t1 = 4 * i
  add $t1, $t1, $s3 # $t1 = address of A[i] (4 * i + $s3)
  lw $t0 , 0($t1) # temp reg $t0 = A[i]
  add $s1, $s2, $t0 # g = h + A[i]
Notes: Spilling registers：寄存器溢出

## Slide 29: What if many variables ?
Spilling registers:
  Putting less commonly used variables (or those needed later) into memory.

## Slide 30
int i;
int A[3];
int j;
FFFF FFFF
0000 0000
i
A
j
PUSH
POP
STACK

## Slide 31
int i,A[3], j;
…
j=A[3];
The result j=?
A
i
A[0]
A[1]
A[2]
A[3]

## Slide 32
Constant or immediate Operands
  Many time a program will use a constant in an operation
    Incrementing index to point to next element of array
    Add the constant 4 to register $s3
    Assuming AddrConstants4 is address pointer of constant 4
lw $t0, AddrConstant4($s1) # $t0=constant 4
add $s3, $s3, $t0 #$s3=$s3+$t0($t0==4)
  Immediate: Other method for adding
  constant 4 to $s3
    Avoids the load instruction
    Offer versions of the instruction
    addi $s3, $s3, 4 #$s3= $s3+ 4
Design Principle 3
  Make the common case fast: (why?) Constant operands occur frequently, it is very common Loading them from memory is very slow
4
….
$s1
AddrConstants 4

## Slide 33
Immediate Operands
An instruction may require a constant as input
An immediate instruction uses a constant number as one
of the inputs (instead of a register operand)
addi $s0, $zero, 1000 # the program has base address
# 1000 and this is saved in $s0
# $zero is a register that always
# equals zero
addi $s1, $s0, 0 # this is the address of variable a
addi $s2, $s0, 4 # this is the address of variable b
addi $s3, $s0, 8 # this is the address of variable c
addi $s4, $s0, 12 # this is the address of variable d[0]

## Slide 34
Recall – Numeric Representations
Decimal 3510
Binary 001000112
Hexadecimal (compact representation)
0x 23 or 23hex
0-15 (decimal)  0-9, a-f (hex)
Dec Binary Hex
0 0000 00
1 0001 01
2 0010 02
3 0011 03
Dec Binary Hex
4 0100 04
5 0101 05
6 0110 06
7 0111 07
Dec Binary Hex
8 1000 08
9 1001 09
10 1010 0a
11 1011 0b
Dec Binary Hex
12 1100 0c
13 1101 0d
14 1110 0e
15 1111 0f

## Slide 35
Name | Example | Comments
32 register | $s0,$s1…… $t0, $t1……. | Fast locations for data. In MIPS, data must be in registers to perform arithmetic.
230 memory words | Memory[0], Memory[4] , …… , Menory[4294967292] | Accessed only by data transfer instructions in MIPS. MIPS uses byte addr. , so sequential word addr. Differ by 4. Memory holds data structures, arrays, and spilled registers.
MIPS operands p59
MIPS assembly language
Category | Instruction | Example | Meaning | Comments
Arithmetic | add | add $s1,$s2,$s3 | $s1=$s2 + $s3 | Three register operands
 | subtract | sub $s1,$s2,$s3 | $s1=$s2－$s3 | Three register operands
 | Add immediate | addi $s1,$s2,100 | $s1=$s2+100 | Used to add constants
Data transfer | load word | lw $s1, 100($s2) | $s1=Memory[$s2+100] | Data from memory to register
 | store word | sw $s1, 100($s2) | Memory[$s2+100]=$s1 | Data from register to memory

## Slide 36: 3.2 Signed and Unsigned Numbers Possible Representations
Sign Magnitude: One's Complement Two's Complement 000 = +0 000 = +0 000 = +0 001 = +1 001 = +1 001 = +1 010 = +2 010 = +2 010 = +2 011 = +3 011 = +3 011 = +3 100 = -0 100 = -3 100 = -4 101 = -1 101 = -2 101 = -3 110 = -2 110 = -1 110 = -2 111 = -3 111 = -0 111 = -1
Issues: number of zeros, ease of operations
Which one is best? Why?

## Slide 37: Numbers and their representation
Number systems
  Radix based systems are dominating
  decimal, octal, binary,…
  b: value of the digit, k: radix, n: digits left of radix point, m: digits right of radix point
  Alternatives, e.g. Roman numbers (or Letter)
Decimal (k=10) -- used by humans
Binary (k=2) -- used by computers
0≤b≤K
(N)k＝(An－1A n－2A n－3…A 1A 0 • A-1A -２A…A –m+1A – m)k
MSB
LSB

## Slide 38: Numbers and their representation
Representation
  ASCII - text characters
    Easy read and write of numbers
    Complex arithmetic (character wise)
  Binary number
    Natural form for computers
    Requires formatting routines for I/O

## Slide 39: Endianness/byte order
Big end：Leftmost
  powerpc
  01 02 = 258
Little end：Rightmost
  X86， ARM, MIPS
  01 02 = 513
Bi-endian
  ARM，PowerPC, Alpha, SPARC

## Slide 40: Signed number representation
First idea:
  Positive and negative numbers
  Take one bit (e.g. 31) as the sign bit
    Problem
    0 0000000 = 0 positive zero!
    1 0000000 = 0 negative zero!
  Each comparison to 0 requires two steps
1's complement
2's complement

## Slide 41: Number types
Integer numbers, unsigned
  Address calculations
  Numbers that can only be positive
Signed numbers
  Positive
  Negative
Floating point numbers
  numeric calculations
  Different grades of precision
    Singe precision (IEEE)
    Double precision (IEEE)
    Quadruple precision

## Slide 42: Number formats
Sign and magnitude
2's complement
1's complement
similar to 2's complement, + 0 & - 0
Biased notation
1000 0000 = minimal negative value(-27)
0111 1111 = maximal positive value (27-1)
Representation
  Binary
  Decimal
  Hexadecimal

## Slide 43: Two's Complement Operations
Negating a two's complement number:
invert all bits and add 1 with end
  remember: “negate” and “invert” are quite different!
Defining : Assume:x＝±0.x-1x-２x-３…x-m OR x＝±xn－1xn－２xn－３xn－4…x0
Converting n bit numbers into numbers with more than n bits:
  MIPS 16 bit immediate gets converted to 32 bits for arithmetic
  copy the most significant bit (the sign bit) into the other bits 0010 -> 0000 0010 1010 -> 1111 1010
Ｘ 0≤X<1
２＋Ｘ＝2－|Ｘ| -1≤X<0
Ｘ 0≤X<2n
2n+1＋Ｘ＝2n+1－|Ｘ| -2n≤X<0
fraction
integer
[X]C＝

## Slide 44: 2's complement for n=3
Only one representation for 0
All numbers less than zero has the MSB = 1
One more negative number than positive number
2n+1＋Ｘ＝2n+1-|Ｘ|
＝ 24 －8
＝(10000-1000)2
＝ 01000
Ex2: 37: 0 0 1 0 0 1 0 1
1 1 0 1 1 0 1 0
1 1 1 1 1 1 1 1
+ 1  1101 1011 (-37)
0 0 0 0 0 0 0 0

## Slide 45: If x<0, how to know its IxI ?
Ex2: -37: 1 1 0 1 1 0 1 1
0 0 1 00 1 0 0
1 1 1 1 1 1 1 1
+ 1  00100101 (37)
0 0 0 0 0 0 0 0

## Slide 46: Why use 2’s complement ? -----natural way to present
Ex1: one sign bit 1’s comlement 2’s complement
  +5 0 1 0 1 0 1 0 1 0101
  -5 1 1 0 1 1 0 1 0 1011
  0 0 0 1 0(2) 1 1 1 1 (-0) 0000 (good)
Problem for 1’s complement
  0001 0011 19
  − 1111 1100 −3
  1 0001 0111 23 —An end-around borrow is produced.
  − 0000 0001 1 —Subtract end-around borrow from result.
  0001 0110 22 —The correct result (19 − (−3) = 22).

## Slide 47: Another good thing for 2’s complement
We don’t need subtraction
EX:
1’s complement 2’s complement
  ------------------------- --------------------------
  0001 0011 19 0001 0011 19
  − 1111 1100 −3 + 1111 1101 -3
  1 0001 0111 23 1 0001 0000 16
  − 0000 0001 1
  0001 0110 22

## Slide 48: More common: use of 2's complement---- negatives have one additional number
(0000 0000 0000 0000 0000 0000 0000 0000)2 =(0)10
(0000 0000 0000 0000 0000 0000 0000 0001)2 =(1)10
………… ………
(0111 1111 1111 1111 1111 1111 1111 1101)2 =( 2，147，483，645)10
(0111 1111 1111 1111 1111 1111 1111 1110)2 =( 2，147，483，646)10
(0111 1111 1111 1111 1111 1111 1111 1111)2 =( 2，147，483，647)10
(1000 0000 0000 0000 0000 0000 0000 0000)2 =(-2，147，483，648)10
(1000 0000 0000 0000 0000 0000 0000 0001)2 =(-2，147，483，647)10
(1000 0000 0000 0000 0000 0000 0000 0010)2 =(-2，147，483，646)10
………… ………
(1111 1111 1111 1111 1111 1111 1111 1101)2 =(-3)10
(1111 1111 1111 1111 1111 1111 1111 1110)2 =(-2)10
(1111 1111 1111 1111 1111 1111 1111 1111)2 =(-1)10

## Slide 49: sign extension (lbu vs. lb)
Sign Extension
e.g. 16 bit numbers to 32 bit numbers
Required for operations with registers(32 bits) and immediate operands (16 bits)
Sign extension
  Take the lower 16 bits as they are
  Copy the highest bit to the remaining 16 bits
  0000 0000 0000 0010 → 2
  0000 0000 0000 0000 0000 0000 0000 0010
  1111 1111 1111 1110 → -2
  1111 1111 1111 1111 1111 1111 1111 1110

## Slide 50: Compare operations
Different compare operations required for both number types
  Signed integer
    slt Set when less than
    slti Set when less than immediate
  Unsigned integer
    sltu Set when less than
    sltiu Set when less than immediate

## Slide 51: Example for Compare
Register $s0
1111 1111 1111 1111 1111 1111 1111 1111
Register $s1
0000 0000 0000 0000 0000 0000 0000 0001
Compared Operations
slt $t0, $s0, $s1
sltu $t0, $s0, $s1
Results
$t0 = 1 (-1 < 1)
$t0 = 0 (4,294,967,295ten > 1ten)

## Slide 52: Effects of Overflow
An exception (interrupt) occurs
  Control jumps to predefined address for exception
  Interrupted address is saved for possible resumption
Don't always want to detect overflow — new MIPS instructions: addu, addiu, subu
note: addiu still sign-extends! note: sltu, sltiu for unsigned comparisons

## Slide 53
2.5 Instruction Formats----Representing instructions
Instructions are represented as 32-bit numbers (one word),
broken into 6 fields
R-type instruction add $t0, $s1, $s2
000000 10001 10010 01000 00000 100000
6 bits 5 bits 5 bits 5 bits 5 bits 6 bits
op rs rt rd shamt funct
opcode source source dest shift amt function
I-type instruction addi $t0, $s1, #8
001000 10001 01000 00000 00000 01000
6 bits 5 bits 5 bits 16 bits
opcode rs rt constant

## Slide 54: Instructions Encoding (3 formats)
R-type
  Add, Sub, Or, And, …
I-type
  LW, SW, BEQ, BNE, ADDi, …
J-type
  J, …
R-type | op | rs | rt | rd | sa | func
I-type | op | rs | rt | immediate |  | 
J-type | op | address |  |  |  | 

## Slide 55: R-type Instruction
R-Type - This group contains all instructions that do not require an immediate value, target offset, memory address displacement, or memory address to specify an operand. This includes arithmetic and logic with all operands in registers, shift instructions, and register direct jump instructions (jalr and jr).
All R-type instructions use opcode 000000.
1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
OP:6 |  |  |  |  |  | Rs:5 |  |  |  |  | Rt:5 |  |  |  |  | Rd:5 |  |  |  |  | Shamt:5 |  |  |  |  | Func:6 |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
add $t0, $s1, $s2
sub $t0, $s1, $s2

## Slide 56
MIPS fields (format) p63
  R-type or R-format
| op | rs | rt | rd | shamt | funct |
  6 bits 5 bits 5 bits 5 bits 5 bits 6 bits
  I-type or I-format
| op | rs | rt | address |
  6 bits 5 bits 5 bits 16 bits
Op : basic operation of the instruction, traditionally called the opcode.
rs: the first register source operand.
rt: the second register source operand.
rd: the register destination operand.
shamt: shift amount.
funct: function,this field selects the specific variant of the operation in the op field.
Region: ±215
Must bear in mind !

## Slide 57: Representing Instruction
All information in computer consists of binary bits
Mapping registers into numbers
  Map registers $s0 to $s7 onto registers 16 to 23
  Map registers $t0 to $t7 onto registers 8 to 15
Ex2.7: Translating assembly into machine instruction
  MIPS code
  add $t0, $s1, $s2  add r8, r17, r18
  Decimal version of machine code
  | 0 | 17 | 18 | 8 | 0 | 32 |
  Binary version of machine code
  | 000000 | 10001 | 10010 | 01000 | 00000 | 100000 |
  6 bits 5 bits 5 bits 5 bits 5 bits 6 bits
Sometime use Hex!

## Slide 58
Design Principle 3
  Good design demands good compromises
All instructions in MIPS have the same length
(fixed encoding)
same length ←--→ single instruction
Other than Variable encoding / mixed encoding (CISC: VAX)

## Slide 59: Ex2.8 Translating assembly into machine instruction
C code:
  A[300] = h + A[300] ; ( Assume: h ---- $s2 base address of A ---- $t1 )
MIPS assembly code:
  lw $t0, 1200($t1) # temporary reg $t0 gets A[300]
  add $t0, $s2, $t0 # temporary reg $t0 gets h + A[300]
  sw $t0, 1200($t1) # stores h + A[300] back into A[300]
MIPS machine language code:
    Decimal version address/
    op rs rt rd shamt funct
  | 35 | 9 | 8 | 1200 |
  | 0 | 18 | 8 | 8 | 0 | 32 |
  | 43 | 9 | 8 | 1200 |
lw
add
sw

## Slide 60
Binary version
  | 100011 | 01001 | 01000 | 0000 0100 1011 0000 |
  | 000000 | 10010 | 01000 | 01000 | 00000 | 100000 |
  | 101011 | 01001 | 01000 | 0000 0100 1011 0000 |
  Note the only difference of the first and last instructions!
Two key principles of today’s computers
  Instructions are represented as numbers
  Programs can be stored in memory like numbers
Store-program
concept
lw
add
sw

## Slide 61
Stored-program concept

## Slide 62
000000 | 01000 | 10010 | 01000 | 00000 | 100000
op rs rt rd shamt funct
add $t0, $t0 , $s2,
00000001000100100100000000100000
Memory addr: 0x40000008
main() {
int *p;
p=0x40000008;
*p+=2
}
000000 | 01000 | 10010 | 01000 | 00000 | 100010
sub $t0, $t0 , $s2
问题：如果这是一个执行程序拳击游戏，该行指令表示您挨打，血(t0)在减少(s2为负数)，当血小于等于0，KO。
用ultraedit将该二进制执行文件修改，让自己不损血，怎么改？

## Slide 63: MIPS operands, assembly and machine language p67
Name | Format | Example |  |  |  |  |  | Comment
add | R | 0 | 18 | 19 | 17 | 0 | 32 | add $s1, $s2, $s3
sub | R | 0 | 18 | 19 | 17 | 0 | 34 | sub $s1, $s2, $s3
addi | I | 8 | 18 | 17 | 100 |  |  | addi $s1,$s2,100
lw | I | 35 | 18 | 17 | 100 |  |  | lw $s1, 100($s2)
sw | I | 43 | 18 | 17 | 100 |  |  | sw $s1, 100($s2)
Field size |  | 6bits | 5bits | 5bits | 5bits | 5bits | 6bits | All MIPS instruction 32 bits
R-format | R | op | rs | rt | rd | shamt | funct | Arithmetic instruction format
I-format | I | op | rs | rt | address |  |  | Data transfer ,branch format
Category | Instruction | Example | Meaning | Comments
Arithmetic | add | add $s1,$s2,$s3 | $s1=$s2 + $s3 | Three register operands
 | subtract | sub $s1,$s2,$s3 | $s1=$s2－$s3 | Three register operands
 | Add immediate | addi $s1,$s2,100 | $s1=$s2+100 | Used to add constants
Data transfer | load word | lw $1, 100($s2) | $s1=Memory[$s2+100] | Data from memory to register
 | store word | sw $s1, 100($s2) | Memory[$s2+100]=$s1 | Data from register to memory
Name | Example | Comments
32 register | $s0,$s1……,$s7 $t0, $t1…….,$t7 | Fast locations for data. In MIPS, data must be in registers to perform arithmetic. Registers $s0-$s7 map to 16-23 and $t0-$t7 map to 8-15.
230 memory words | Memory[0], Memory[4] , …… , Menory[4294967292] | Accessed only by data transfer instructions in MIPS. MIPS uses byte addr., so sequential word addr. Differ by 4. Memory holds data structures,arrays, and spilled registers.

## Slide 64
2.6 Logical Operations
Logical ops C operators Java operators MIPS instr
Shift Left << << sll
Shift Right >> >>> srl
Bit-by-bit AND & & and, andi
Bit-by-bit OR | | or, ori
Bit-by-bit NOT ~ ~ nor
Sll: Shift Left Logical
Srl: Shift Right Logical

## Slide 65: SLL (shift Left Logical)
  Move all the bits in a word to left or right, filling emptied bits with 0
  Shifting left by i is same result as multiplying by 2i
  0000 0000 0000 0000 0000 0000 0000 1001 (9)10
  0000 0000 0000 0000 0000 0000 1001 0000 Shift left 4
  (9×24 = 9×16=144)10
  sll $t2, $s0, 4 # $t2 = reg $s0 << 4 bit
op | rs | rt | rd | shamt | funct
0 | 0 | 16 | 10 | 4 | 0

## Slide 66: And operator
  It is bit-by-bit
    Result=1 : both bits of the operands are 1
  Example:
  $t2: 0000 0000 0000 0000 0000 1101 0000 0000
  $t1: 0000 0000 0000 0000 0011 1100 0000 0000
  and $t0, $t1, $t2 #reg $t0=reg $t1 & reg $t2
  $t0 Result:
  0000 0000 0000 0000 0000 1100 0000 0000

## Slide 67: OR operator
It is bit-by-bit
    Result=1 : either bits of the operands is 1
  $t2: 0000 0000 0000 0000 0000 1101 0000 0000
  $t1: 0000 0000 0000 0000 0011 1100 0000 0000
  or $t0, $t1, $t2 # $t0 = $t1 | $t2
  $t0 Result:
  0000 0000 0000 0000 0011 1101 0000 0000

## Slide 68: NOR operator
  NOT(A OR B)
    A NOR 0 =NOT(A OR 0) = NOT(A)
  $t1: 0000 0000 0000 0000 0011 1100 0000 0000
  $t3: 0000 0000 0000 0000 0000 0000 0000 0000
  nor $t0, $t1, $t3 # $t0 = ~ (reg $t1 | reg $t3)
  $t0 Result:
  1111 1111 1111 1111 1100 0011 1111 1111

## Slide 69: MIPS operands p71
MIPS assembly language
Name | Example | Comments
32 register | $s0,$s1……,$s7 $t0, $t1…….,$t7 | Fast locations for data. In MIPS, data must be in registers to perform arithmetic. Registers $s0-$s7 map to 16-23 and $t0-$t7 map to 8-15.
230 memory words | Memory[0], Memory[4] , …… , Menory[4294967292] | Accessed only by data transfer instructions in MIPS. MIPS uses byte addr., so sequential word addr. Differ by 4. Memory holds data structures,arrays, and spilled registers.
Category | Instruction | Example | Meaning | Comments
Arithmetic | add | Add $s1,$s2,$s3 | $s1=$s2 + $s3 | Three register operands
 | subtract | Sub $s1,$s2,$s3 | $s1=$s2－$s3 | Three register operands
 | Add immediate | addi $s1,$s2,100 | $s1=$s2+100 | +constants; overflow detected
Data transfer | load word | lw $1, 100($s2) | $s1=Memory[$s2+100] | Data from memory to register
 | store word | sw $s1, 100($s2) | Memory[$s2+100]=$s1 | Data from register to memory
logical | and | and $s1,$s2,$s3 | $s1=$s2 & $s3 | three reg. operands;bit-by-bit AND
 | or | or $s1,$s2,$s3 | $s1=$s2 ¦ $s3 | three reg. operands;bit-by-bit OR
 | nor | nor $s1,$s2,$s3 | $s1=~($s2 ¦ $s3) | three reg. operands;bit-by-bit NOR
 | and immediate | addi $s1,$s2,100 | $s1=$s2 & 100 | Bit-by-bit AND reg with constant
 | or immediate | ori $s1,$s2,100 | $s1=$s2 ¦ 100 | Bit-by-bit OR reg with constant
 | shift left logical | sll $s1,$s2,10 | $s1=$s2 << 10 | Shift left by constant
 | shift right logical | srl $s1,$s2,10 | $s1=$s2 >> 10 | Shift right by constant

## Slide 70: 2.7 Instr. For Making Decision
Based on the input data and the value created during computation, different instructions execute.
Unconditional branch
  J
  JR, JAL
Conditional branches
  BEQ, BNE
  SLT
  …

## Slide 71: Control Instructions
Conditional branch
  Jump to instruction L1 if reg1 equals reg2:
beq $s1, $s2, L1
  Jump to instruction L1 if reg1 not equals reg2:
bne $s1, $s2, L1
  slt $t0, $s1, $s2 (set-on-less-than)
beq | 000100 | rs | rt | imm |  | if (rs == rt) PC+=4 + (sign_extend)imm <<2; | PC+=4
bne | 000101 | rs | rt | imm |  | if (rs != rt) PC+=4 + (sign_extend)imm <<2; | PC+=4
slt | 000000 | rs | rt | rd | 00000101010 | if (rs <= rt) rd = 1 else rd = 0 | 

## Slide 72: Control Instructions
Target PC
  (PC+4)+ (sign_extend)imm <<2
  It’s called PC-relative addressing
  Displacement(immediate) range:
  -215 ~ 215 - 1
beq | 000100 | rs | rt | imm |  | if (rs == rt) PC+=4 + (sign_extend)imm <<2; | PC+=4
bne | 000101 | rs | rt | imm |  | if (rs != rt) PC+=4 + (sign_extend)imm <<2; | PC+=4

## Slide 73: Example 2.9
Compiling an if statement to a branch
( Assume: f ~ j ---- $s0 ~ $s4 )
  C code:
  if ( i = = j ) goto L1 ;
  f = g + h ;
  L1: f = f - i ;
  MIPS assembly code:
  beq $s3, $s4, L1 # go to L1 if i equals j
  add $s0, $s1, $s2 # f = g + h ( skipped if i equals j )
  L1: sub $s0, $s0, $s3 # f = f - i ( always executed )

## Slide 74: Control Instructions
Unconditional branch:
  j L1
  jal label
  jr $s0
J-type | op | address |  |  |  |  |  |  |  |  |  | 
j | 000010 | address |  |  |  |  |  |  |  |  | PC = (PC+4)[31..28],address<<2 | 
jal | 000011 | address |  |  |  |  |  |  |  |  | PC = (PC+4)[31..28],address<<2 ; $31 = PC+4 | 
jr | 000000 | rs |  | 00000 |  | 00000 |  | 00000 |  | 001000 | PC = rs | 

## Slide 75: J: Jump instruction
Execute:
  PC = label
    Direct addressing. but impossible, why?
  PC = ((PC+4) & 0xF000_0000) | (label << 2)
    Pseudodirect addressing
  PC: Program Count
    The register that always holds the address of the current instruction being executed.
1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
OP:6 |  |  |  |  |  | Addr:26 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
J label

## Slide 76: J-type
J-Type - This group consists of the two direct jump instructions (j and jal). These instructions require a memory address to specify their operand.
J-type instructions use opcodes 00001x.
JAL: Jump and Link
  Execute:
    1. $ra = PC+4;
    2. J label;
JR $r (R-type )
  Execute:
    PC = $r

## Slide 77: Exercise
Assemble
    ADD $S2, $T8, $T0
    LW $S0, $S1(-123)
    SW $RA, $SP(123)
    For: BEQ $T0, $T1, For
Un-assemble
    02488824
    8E30FF85
    AFBF007B
    1109FFFF

## Slide 78
Control Instructions
J LABEL
beq I, j, Equal
sub f, g, h
j Exit
Equal: add f, g, h
Exit:
Convert to assembly:
if (i == j)
f = g+h;
else
f = g-h;
i==j?
F=g+h
F=g - h
Y
N
Exit:
Ex2.10

## Slide 79: Conditional branch
(1)
=
(2)
(3)
Y
N
(1)
(2)
(3)
(1) beq $s3, $s4, Exit
(2) add $s0, $s1, $s2
Exit: (3)

## Slide 80: BEQ & BNE
Beq $r1, $r2, Label
  if($r1 == $r2) goto Label
    goto Label: PC=PC+4+(Label<<2)
        -- PC relative addressing
        -- $r: any register
Bne $r1, $r2, Label
  if($r1 != $r2) goto Label

## Slide 81: If-Then-Else
Ex2.11
(1)
bne $s3, $s4, Else
(2) add $s0, $s1, $s2
j Exit
Else: (3)sub $s0, $s1, $s2
Exit: (4)
(1)
< >?
(2)
(4)
Y
N
(3)
(1)
(2)
(3)
(4)
Y
Memory

## Slide 82: SLT: set less than
Most Popular Compare Operation
SLT $rd, $r1, $r2
  if($r1 < $r2) $rd = 1; else $rd = 0;
1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
OP:6 |  |  |  |  |  | Rs:5 |  |  |  |  | Rt:5 |  |  |  |  | Rd:5 |  |  |  |  | Shamt:5 |  |  |  |  | Func:6 |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 0 | 1 | 0 | 1 | 0
slt $t0, $s1, $s2

## Slide 83: Control Flow
if ($s1 < $s2) then
…(1)
else
…(2)
2
Slt $t0, $s1, $s2
bne $t0, $zero, (1)
…(2)
j exit
(1) …(1)
Exit:
……
<
(2)
Y
N
(1)
Notes: Board work: Binary Numbers

## Slide 84: Control Flow
if ($s1 > $s2) then
…(1)
else
…(2)
2
Slt $t0, $s2, $s1
bne $t0, $zero, (1)
…(2)
j exit
(1) …(1)
Exit:
……
>
(2)
Y
N
(1)
Notes: Board work: Binary Numbers

## Slide 85: SLT
SLT $rd, $r1, $r2
  if($rs<$rt)$rd=1; else $rd=0;
if($r1 < $r2)goto lable
  Blt $r1, $r2, label
if($r1 > $r2)goto lable
  Bgt $r1, $r2, label
if($r1<=$r2)goto lable
  Ble $r1, $r2, label
if($r1>=$r2)goto lable
  Bge $r1, $r2, label
SLT $at, $r1, $r2
Bne $at, $zero, label
SLT $at, $r2, $r1
Bne $at, $zero, label
SLT $at, $r2, $r1
Beq $at, $zero, label
SLT $at, $r1, $r2
Beq $at, $zero, label
Pseudo
instruction

## Slide 86: Pseudo instruction
These instructions need not be implemented in hardware; however, their appearance in assembly language simplifies translation and programming.
  When considering performance you should count real instructions.
e.g. ( $r, $r1, $r2: any register)
  Move $r1, $r2 //$r1=$r2
  Beqz $r, label
  ……
Add $r1, $r2, $zero
Beq $r, $zero, label

## Slide 87: I-Type
This group includes instructions with an immediate operand
  branch instructions
  load and store instructions
In the MIPS architecture, all memory accesses are handled by the main processor, so coprocessor load and store instructions are included in this group.
All opcodes except 000000, 00001x, and 0100xx are used for I-type instructions.

## Slide 88: I-type Instruction
I: immediate
  ALU Register-Immediate operation
1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
OP:6 |  |  |  |  |  | Rs:5 |  |  |  |  | Rd:5 |  |  |  |  | Data:16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
addi $t0, $s1, #4

## Slide 89: I-type Instruction
I: immediate
  Lw/Sw instruction
1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
OP:6 |  |  |  |  |  | Rs:5 |  |  |  |  | Rd:5 |  |  |  |  | Data:16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
lw $t0, 0($s1)

## Slide 90: I-type Instruction
I: immediate
  Lw/Sw instruction
  Notice that sw has NO destination register
1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
OP:6 |  |  |  |  |  | Rs:5 |  |  |  |  | Rd:5 |  |  |  |  | Data:16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
sw $t0, 0($s1)

## Slide 91: I-type Instruction
I: immediate
  Beq, Bne
1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
OP:6 |  |  |  |  |  | Rs:5 |  |  |  |  | Rt:5 |  |  |  |  | Data:16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
beq $t0, $s1, exit

## Slide 92: I-type Instruction
I: immediate
1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
OP:6 |  |  |  |  |  | Rs:5 |  |  |  |  | Rd:5 |  |  |  |  | Data:16 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
beq $t0, $s1, exit
lw $t0, 0($s1)
sw $t0, 0($s1)

## Slide 93: Ex 2.11 Supports LOOPs
Compiling a loop with variable array index
( Assume: g ~ j ---- $s1 ~ $s4 base of A[i] ---- $s5)
  C code:
  Loop: g = g + A[i] ; // A is an array of 100 words
  i = i + j ;
  if ( i != h ) goto Loop ;
  MIPS assembly code:
  Loop: add $t1, $s3, $s3 # temp reg $t1 = 2 * i
  add $t1, $t1, $t1 # temp reg $t1 = 4 * i
  add $t1, $t1, $s5 # $t1 = address of A[i]
  lw $t0, 0($t1) # temp reg $t0 = A[i]
  add $s1, $s1, $t0 # g = g + A[i]
  add $s3, $s3, $s4 # i = i + j
  bne $s3, $s2, Loop # go to Loop if i != h

## Slide 94
Ex2.12 While statement
Convert to assembly:
while (save[i] <> k)
i += 1;
i and k are in $s3 and $s5 and
base of array save[] is in $s6

## Slide 95
While statement
Convert to assembly:
while (sa[i] <> k) i : $s3
i += 1; k : $s5
Sa[] : base of array is in $s6
Loop: sll $t1, $s3, 2 ; t1i*4
add $t1, $t1, $s6 ; t1  sa[i] address
lw $t0, 0($t1) ; t0  sa[i]
beq $t0, $s5, Exit ; sa[i] == K, go Exit
addi $s3, $s3, 1 ; ii+1
j Loop
Exit:

## Slide 96: For, do while, while
C code
For (i=0;i<100;i++）
  xxx（1行汇编）
MIPS code
ADD R4, R0, R0
LOOP: SLT R3, R4, 100
BEQ R3, R0, exit
Xxx
ADD R4, R4, #1
J LOOP
Exit:
100次循环运行，运行时间=1+5*100+2
C code
i=0;
Do {
  xxx（1行汇编）
  i++;
  } while (i<100);
MIPS code
ADD R4, R0, R0
LOOP: Xxx
Add R4, R4, #1
SLT R3, 99, R4
BEQ R3, R0, LOOP
Exit:
100次循环运行，运行时间=1+4*100
C code
i=0;
while (i<100); {
  xxx（1行汇编）
  i++;
  }
MIPS code
ADD R4, R0, R0
LOOP: SLT R3, R4, 100
BEQ R3, R0, exit
LOOP: Xxx
Add R4, R4, #1
J LOOP
Exit:
100次循环运行，运行时间=1+5*100+2
虽然直接从C翻译到汇编，性能有差距，然而通过编译技术可以实现相同的性能优化

## Slide 97: 2.14 Case/Switch
  switch ( k ) {
  case 0 : f = i + j ; break ; /* k = 0 */
  case 1 : f = g + h ; break ; /* k = 1 */
  case 2 : f = g - h ; break ; /* k = 2 */
  case 3 : f = i - j ; break ; /* k = 3 */
  }

## Slide 98: JR instruction & jump address table
Jump with register content
jr $r
jump address table
K=0 | P1 address
K=1 | P2 address
K=2 | P3 address
K=3 | P4 address
$t4
 | …………
P1 address | Program 1
 | …………
P2 address | Program 2
 | …………
P3 address | Program 3
 | …………
P4 address | Program 3
 | …………
$r←$t4+4*K

## Slide 99
  MIPS assembly code:
  slt $t3, $s5, $zero # test if k < 0
  bne $t3, $zero, Exit # if k < 0, go to Exit
  slt $t3, $s5, $t2 # test if k < 4
  beq $t3, $zero, Exit # if k >= 4, go to Exit
  add $t1, $s5, $s5 # temp reg $t1 = 2 * k (0<=k<=3)
  add $t1, $t1, $t1 # temp reg $t1 = 4 * k
  add $t1, $t1, $t4 # $t1 = address of JumpTable[k]
  lw $t0, 0($t1) # temp reg $t0 = JumpTable[k]
  jr $t0 # jump based on register $t0
L0: add $s0, $s3, $s4 # k = 0 so f gets i + j
  j Exit # end of this case so go to Exit
L1: add $s0, $s1, $s2 # k = 1 so f gets g + h
  j Exit # end of this case so go to Exit
L2: sub $s0, $s1, $s2 # k = 2 so f gets g - h
  j Exit # end of this case so go to Exit
L3: sub $s0, $s3, $s4 # k = 3 so f gets i - j
  Exit: # end of switch statement
jump address table
$t1= $t4+4 * k:
L0:address
L1:address
L2: address
L3:address

## Slide 100: 2.8 Supporting Procedures in Computer Hardware
Procedure/function be used to structure programs
  A stored subroutine that performs a specific task based on the parameters with which it is provided
    easier to understand, allow code to be reused
Six step
  Place Parameters in a place where the procedure can access them
  Transfer control to the procedure
  Acquire the storage resources needed for the procedure
  Perform the desired task
  Place the result value in a place where the calling program can access it
  Return control to the point of origin

## Slide 101
Registers for procedure calling
  $a0 ~ $a3: four argument registers to pass parameters
  $v0 ~ $v1: two value registers to return values
  $ra: one return address register to return to origin point
Instruction for procedures: jal ( jump-and-link )
Caller jal ProcedureAddress
Callee jr $ra
Using more registers
  Stack: ideal data structure for spilling registers
    Push, pop
    Stack pointer ( $sp )
PC+4→$ra
Special registers

## Slide 102
Registers
The 32 MIPS registers are partitioned as follows:
  Register 0 : $zero always stores the constant 0
  Regs 2-3 : $v0, $v1 return values of a procedure
  Regs 4-7 : $a0-$a3 input arguments to a procedure
  Regs 8-15 : $t0-$t7 temporaries
  Regs 16-23: $s0-$s7 variables
  Regs 24-25: $t8-$t9 more temporaries
  Reg 28 : $gp global pointer
  Reg 29 : $sp stack pointer
  Reg 30 : $fp frame pointer
  Reg 31 : $ra return address

## Slide 103
Jump-and-Link
A special register (storage not part of the register file) maintains the
address of the instruction currently being executed – this is the
program counter (PC)
The procedure call is executed by invoking the jump-and-link (jal)
instruction – the current PC (actually, PC+4) is saved in the register
$ra and we jump to the procedure’s address (the PC is accordingly
set to this address)
jal NewProcedureAddress
Since jal may over-write a relevant value in $ra, it must be saved
somewhere (in memory?) before invoking the jal instruction
How do we return control back to the caller after completing the
callee procedure?

## Slide 104
The Stack
The register scratchpad for a procedure seems volatile –
it seems to disappear every time we switch procedures –
a procedure’s values are therefore backed up in memory
on a stack
High address
Low address
Proc A’s values
Proc B’s values
Proc C’s values
…
Stack grows
this way
Proc A
call Proc B
…
call Proc C
…
return
return
return

## Slide 105
Storage Management on a Call/Return
A new procedure must create space for all its variables on the stack
Before executing the jal, the caller or callee must save relevant values in
$s0-$s7, $a0-$a3, $ra, temps（important $t ） into its own stack space
Arguments are copied into $a0-$a3; the jal is executed
After the callee creates stack space, it updates the value of $sp
Once the callee finishes, it copies the return value into $v0, frees
up stack space, and $sp is incremented
On return, the caller may bring in its stack values, ra, temps into registers
The responsibility for copies between stack and registers may fall
upon either the caller or the callee

## Slide 106: Saves on Stack
Caller saved
  $a0-a3 -- old arguments must be saved before setting new arguments for the callee
  $ra -- must be saved before the jal instruction over-writes this value
  $t0-t9 -- if you plan to use your temps after the return, save them note that callees are free to use temps as they please
  You need not save $s0-s7 as the callee will take care of them
Callee saved
  $s0-s7 -- before the callee uses such a register, it must save the old contents since the caller will usually need it on return
  local variables -- space is also created on the stack for variables local to that procedure

## Slide 107
Ex2.15 Procedure call
int leaf_example (int g, int h, int i, int j)
{
int f ;
f = (g + h) – (i + j);
return f;
}
($t1)
($t0)
($s0)
$sp(-12)
High address
Low address
Assume: t0: g+h
t1: i+j
s0: ( g+h) – (I + j)

## Slide 108
Example 2.15
int leaf_example (int g, int h, int i, int j)
{
int f ;
f = (g + h) – (i + j);
return f;
}
leaf_example:
addi $sp, $sp, -12
sw $t1, 8($sp)
sw $t0, 4($sp)
sw $s0, 0($sp)
add $t0, $a0, $a1
add $t1, $a2, $a3
sub $s0, $t0, $t1
add $v0, $s0, $zero
lw $s0, 0($sp)
lw $t0, 4($sp)
lw $t1, 8($sp)
addi $sp, $sp, 12
jr $ra
Notes:
In this example, callee protect All the registers it will use avoiding any register change for caller ----a conservative way
The caller took care of saving its $ra and
$a0-$a3.

## Slide 109
Example 2.16 Nested procedure
int fact (int n)
{
if (n < 1) return (1);
else return (n * fact(n-1));
}
Assume n = 2 -------- $a0
Assume
MAIN program:
jal fact
1000 :
2000: L1

## Slide 110
Example 2.16
int fact (int n)
{
if (n < 1) return (1);
else return (n * fact(n-1));
}
fact:
addi $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
slti $t0, $a0, 1
beq $t0, $zero, L1
addi $v0, $zero, 1
addi $sp, $sp, 8
jr $ra
L1:
addi $a0, $a0, -1
jal fact
2000: lw $a0, 0($sp)
lw $ra, 4($sp)
addi $sp, $sp, 8
mul $v0, $a0, $v0
jr $ra
Notes:
The caller saves $a0 and $ra
in its stack space.
Temps are never saved.

## Slide 111
SP
SP-16
1000
2
1
2000
1000
2
1
2000
SP-16
1000
2
SP-8
初始 主程序第一次 第一次递归调用 第二次递归调用 N<1时
CALL FACT FACT FACT
SP-24
1000
2
1
2000
2000
0

## Slide 112: Disadvantages of recursion
Use too much resource，to protect the processor status，recursion may result in stack overflow.
Need push and pop，takes a lot of memory space leading to inefficient usage of memory.
How to avoid ? use loop instead of recursion.

## Slide 113: Stack allocation before, during and after procedure call
$fp→
$sp→
$fp→
$sp→
$fp→
$sp→
Saved argument
Registers (if any)
Saved return address
Local arrays and
structures(if any)
High address
Low address
The space allocated on stack by a procedure is termed the activation
record (includes saved values and data local to the procedure)
frame pointer points to the start of the record
stack pointer points to the end – variable addresses are specified relative to $fp as $sp may change during the execution of the procedure

## Slide 114
Procedure frame
  The segment of stack containing a procedure’s saved registers and local variables
Frame pointer ( $fp )
  $fp offers a stable base register, denoting the location of saved register and local variables for a given procedure
  Adjust stack only on entry and exit of procedure to avoid $fp changed
Storage class of C variables
  automatic
  static
Global pointer ( $gp ) points to static variables (静态变量 )

## Slide 115
Memory Organization
$gp points to area in memory that saves global variables
Dynamically allocated storage (with malloc()) is placed on the heap
Stack
Dynamic data (heap)
Static data (globals)
Text (instructions)
Higher address
lower address

## Slide 116: Memory Organization
Addresses are software convention
$gp should be set properly to access the static data easily, here which will cover the range from 10000000x to 1000ffffx through $gp +/- 16 bit displacement.

## Slide 117: data
Global
Static
Automatic
Const
Array
  Int a[4];
  Int *p=malloc(4* sizeof （int） )
Data segment
Data segment
Stack
Data segment
Array
  Stack
  heap

## Slide 118: MIPS operands
Name | Example | Comment
32 registers | $s0-$s7,$t0-$t9. $zero,$a0-$a3,$v0-$v1, | Fast locations for data. In MIPS, data must be in registers to perform arithmetic. MIPS register $zero always equals 0. $gp(28) is the global pointer, $sp(29) is the stack pointer, $fp(30) is the frame pointer, and $ra(31) is the return address.
230 memory words | Memory[0] Memory[4]…… Memory[4294967292] | Accessed only by data transfer instructions. MIPS uses byte addresses, so sequential word addresses differ by 4. Memory holds data structures, arrays, and spilled registers, such as those saved on procedure calls.
Name | Register no. | Usage | Preserved on call
$zero | 0 | The constant value 0 | n,.a.
$v0-$v1 | 2-3 | Values for results and expression evaluation | no
$a0-$a3 | 4-7 | Arguments | no
$t0-$t7 | 8-15 | Temporaries | no
$s0-$s7 | 16-23 | Saved | yes
$t8-$t9 | 24-25 | More temporaries | no
$gp | 28 | Global pointer | yes
$sp | 29 | Stack pointer | yes
$fp | 30 | Framer pointer | yes
$ra | 31 | Return address | yes

## Slide 119: MIPS assembly language p89
Category | Instruction | Example | Meaning | Comments
Arithmetic | add | Add $s1,$s2,$s3 | $s1=$s2 + $s3 | Three register operands
 | subtract | Sub $s1,$s2,$s3 | $s1=$s2－$s3 | Three register operands
Data transfer | load word | lw $1, 100($s2) | $s1=Memory[$s2+100] | Data from memory to register
 | store word | sw $s1, 100($s2) | Memory[$s2+100]=$s1 | Data from register to memory
logical | and | and $s1,$s2,$s3 | $s1=$s2 & $s3 | three reg. operands;bit-by-bit AND
 | or | or $s1,$s2,$s3 | $s1=$s2 ¦ $s3 | three reg. operands;bit-by-bit OR
 | nor | nor $s1,$s2,$s3 | $s1=~($s2 ¦ $s3) | three reg. operands;bit-by-bit NOR
 | and immediate | addi $s1,$s2,100 | $s1=$s2 & 100 | Bit-by-bit AND reg with constant
 | or immediate | ori $s1,$s2,100 | $s1=$s2 ¦ 100 | Bit-by-bit OR reg with constant
 | shift left logical | sll $s1,$s2,10 | $s1=$s2 << 10 | Shift left by constant
 | shift right logical | srl $s1,$s2,10 | $s1=$s2 >> 10 | Shift right by constant
Conditional branch | branch on equal | beq $s1,$s2,L | If($s1==$s2) go to L | Equal test and branch
 | branch not eaqal | bne $s1,$s2,L | If($s1!=$s2) go to L | Not equal test and branch
 | set on less than | slt $s1,$s2,$s3 | If($s2<$s3) $s1=1 Else $s1=0 | Compare less than;used with beq, bne
 | set on less than immediate | slt $s1,$s2100 | If($s2<100) $s1=1 Else $s1=0 | Compare less than immediate; used with beq, bne
Uncondition-al jump | jump | j L | go to L | Jump to target address
 | jump register | jr $ra | go to $ra | For procedure return
 | jump and link | jal L | $ra=PC+4; go to L | For procedure call

## Slide 120: MIPS machine language
Name | Format | Example |  |  |  |  |  | Comment
add | R | 0 | 18 | 19 | 17 | 0 | 32 | add $s1, $s2, $s3
sub | R | 0 | 18 | 19 | 17 | 0 | 34 | sub $s1, $s2, $s3
lw | I | 35 | 18 | 17 | 100 |  |  | lw $s1, 100($s2)
sw | I | 43 | 18 | 17 | 100 |  |  | sw $s1, 100($s2)
and | R | 0 | 18 | 19 | 17 | 0 | 36 | and $s1, $s2, $s3
or | R | 0 | 18 | 19 | 17 | 0 | 37 | or $s1, $s2, $s3
nor | R | 0 | 18 | 19 | 17 | 0 | 39 | nor $s1, $s2, $s3
addi | I | 8 | 18 | 17 | 100 |  |  | addi $s1, $s2,100
ori | I | 13 | 18 | 17 | 100 |  |  | ori $s1, $s2,100
sll | R | 0 | 0 | 18 | 17 | 10 | 0 | sll $s1, $s2,10
srl | R | 0 | 0 | 18 | 17 | 10 | 2 | srl $s1, $s2,10
beq | I | 4 | 17 | 18 | 25 |  |  | beq $s1, $s2,100
bne | I | 5 | 17 | 18 | 25 |  |  | bne $s1, $s2,100
slt | R | 0 | 18 | 19 | 17 | 0 | 42 | slt $s1, $s2,$s3
j | J | 2 | 2500 |  |  |  |  | j 10000(see section 2.9)
jr | R | 0 | 31 | 0 | 0 | 0 | 8 | j Sra
jal | J | 3 | 2500 |  |  |  |  | jar 10000(see section 2.9)
Field size |  | 6bits | 5bits | 5bits | 5bits | 5bits | 6bits | All MIPS instruction 32 bits
R-format | R | op | rs | rt | rd | shamt | funct | Arithmetic instruction format
i-format | I | op | rs | rt | address |  |  | Data transfer ,branch format

## Slide 121
Summerise of procedure
The jal instruction is used to jump to the procedure and
save the current PC (+4) into the return address register
Arguments are passed in $a0-$a3; return values in $v0-$v1
Since the callee may over-write the caller’s registers,
relevant values may have to be copied into memory
Each procedure may also require memory space for
local variables – a stack is used to organize the memory
needs for each procedure

## Slide 122
x: $s1
y: $s2
temp：$t7
Jal B
i: $s2
j: $s3
Jal C
A
B
C
A:
move $a0, $s1
move $a1, $s2
move $s3, $t7
Jal B
use v0， v1
move $t7, $s3 ;restore $t7
B：
Add $sp, $sp, -20 ;apply space
Push $ra, $a0, &a1 ;caller save
Push $s2, $s3, ;callee save
B-func1
Jal C ; B-function
B-func2
Pop $s2, $s3,
Pop $ra, $a0, $a1
Add $sp, $sp, +20 ;release STspace
Move v0, ? ;return value
Jr $ra
caller save $t0 ~ $t7 if the content is important and not want to be modified.
Note： B is callee to A, but caller to C.