## Slide 1
Computer Organization & Design
Hardware Software Interface
Xiaohong Jiang

## Slide 2
Recap
The jal instruction is used to jump to the procedure and
save the current PC (+4) into the return address register
Arguments are passed in $a0-$a3; return values in $v0-$v1
Since the callee may over-write the caller’s registers,
relevant values may have to be copied into memory
Each procedure may also require memory space for
local variables – a stack is used to organize the memory
needs for each procedure

## Slide 3: Memory Organization
Stack
Dynamic data (heap)
Static data (globals)
Text (instructions)
The space allocated on stack by a procedure is termed the activation record (includes saved values and data local to the procedure)
frame pointer points to the start of the record and stack pointer points to the end – variable addresses are specified relative to $fp as $sp may change during the execution of the procedure
$gp points to area in memory that saves global variables
Dynamically allocated storage (with malloc()) is placed on the heap

## Slide 4: 2.9 Communicating with People Beyond Numbers
ASCII ( American Standard Code for Information Interchange )
Instructions for moving bytes in MIPS
  Load byte ( lb ): lb $t0, 0($sp) # read byte from source
  Store byte ( sb ): sb $t0, 0($sp) # write byte to destination
Three choices for representing a string
  Place the length of the string in the first position
  An accompanying variable has the length
  A character in the last position to mark the end of a string
C uses the third choice
  Terminate a string with a byte whose value is 0 ( null in ASCII )

## Slide 5: Example 2.17
Convert to assembly:
int strcpy (char x[], char y[])
{
int i;
i=0;
while ((x[i] = y[i]) != `\0’)
i += 1;
return i;
}
Assuming:
$a1: starting address of y[i]
$a0: starting address of x[i]
$s0: i

## Slide 6
Example
Convert to assembly:
int strcpy (char x[], char y[])
{
int i;
i=0;
while ((x[i] = y[i]) != `\0’)
i ++;
return i
}
strcpy:
addi $sp, $sp, -4
sw $s0, 0($sp)
add $s0, $zero, $zero
L1: add $t1, $s0, $a1
lb $t2, 0($t1)
add $t3, $s0, $a0
sb $t2, 0($t3)
addi $s0, $s0, 1
bne $t2, $zero, L1
addi $v0, $s0, -1
lw $s0, 0($sp)
addi $sp, $sp, 4
jr $ra
Assuming:
$a1: starting address of y[i]
$a0: starting address of x[i]
$s0: i

## Slide 7: 2.10 MIPS Addressing for 32-Bit Immediate and Addresses
32-Bit Immediate addressing
  most constants is short and fit into 16-bit field
How to deal with immediate longer than 16 bits?

## Slide 8: Large Constants
Immediate instructions can only specify 16-bit constants
The lui instruction is used to store a 16-bit constant into the upper 16 bits of a register… thus, two immediate instructions are used to specify a 32-bit constant
The destination PC-address in a conditional branch is specified as a 16-bit constant, relative to the current PC
A jump (j) instruction can specify a 26-bit constant; if more bits are required, the jump-register (jr) instruction is used

## Slide 9: Load Upper Immediate

## Slide 10: Larger Constants?

## Slide 11: Addressing in branches and jumps
Why?
For jumps: J-format
    j 10000 # go to location 10000
  | 2 | 10000 |
  6 bits 26 bits
    Pseudo-direct addressing
    26 bits of the instruction concatenated with the upper 4 bits of PC
For branches:
    bne $s0, $s1, Exit # go to Exit if $s0 != $s1
  | 5 | 16 | 17 | Exit |
  6 bits 5 bits 5 bits 16 bits
    PC-relative addressing
    PC = (PC + 4) + Branch address

## Slide 12: Ex 2.20 Show branch offset in machine
C language: while (save[i]==k) i=i+j; MIPS assembler code in Example 2.12:
  Loop: add $t1, $s3, $s3 # temp reg $t1 = 2 * i
  add $t1, $t1, $t1 # temp reg $t1 = 4 * i
  add $t1, $t1, $s6 # $t1 = address of save[i]
  lw $t0, 0($t1) # temp reg $t0 = save[i]
  bne $t0, $s5, Exit # go to Exit if save[i] != k
  add $s3, $s3, $s4 # i = i + j
  j Loop # go to Loop
  Exit:
Assume: $s6 save the starting address of array save .
$s5 keep the value of K.

## Slide 13
  Assembled instructions and their addresses:
80000 | 0 | 19 | 19 | 9 | 0 | 32 |
80004 | 0 | 9 | 9 | 9 | 0 | 32 |
80008 | 0 | 9 | 22 | 9 | 0 | 32 |
80012 | 35 | 9 | 8 | 0 |
80016 | 5 | 8 | 21 | 2 (8) |
80020 | 0 | 19 | 20 | 19 | 0 | 32 |
80024 | 2 | 20000 (80000) |
80028 . . .
  Modification:
    All MIPS instructions are 4 bytes long
    PC-relative addressing refers to the number of words
    The address field at 80016 above should be 2 instead of 8
add
add
add
Lw
bne
add
j
PC+4+offset=80020 + 8
How about PC offset is larger than 16 bits ?

## Slide 14: Branching far away
Example 2.21
  Given a branch:
  beq $s0, $s1, L1
While branch target is far away
  Inserts an unconditional jump to target
  Invert the condition so that the branch decides whether to skip the jump
  Rewrite it to offer a much greater branching distance:
    bne $s0, $s1, L2
    j L1
    L2:

## Slide 15: MIPS addressing mode summary
Register addressing:
    add $s0, $s0, $s0
Base or displacement addressing:
    lw $s1, 0($s0)
Immediate addressing:
    addi $s0,$s0, 4
PC-relative addressing:
    beq $s0,$s1, L1 PC+4+L1
Pseudodirect addressing:
    j Address1
    [PC+4](31..28) ##Address1

## Slide 16: Five MIPS addressing modes

## Slide 17: Ex 2.22 Decoding machine code
Machine instruction
( Bits: 31 28 26 5 2 0 )
  0000 0000 1010 1111 1000 0000 0010 0000
Decoding
    Determine the operation from opcode
    op: 000000  R-format instruction
    op rs rt rd shamt funct
  | 000000 | 00101 | 01111 | 10000 | 00000 | 100000 |
    5 15 16 add
    Determine other fields
    rs: $a1; rt: $t7; rd: $s0 P88
    Show the assembly instruction
    add $s0, $a1, $t7 (Note: add rd,rs,rt)
$zero 0
$at 1
$v0-$v1 2-3
$a0-$a3 4-7
$t0-$t7 8-15
$s0-$s7 16-23
$t8-$t9 24-25
$k0-$k1 26-27
$gp 28
$sp 29
$fp 30
$ra 31

## Slide 18: Summary of MIPS architecture in Chapter 2 P105
MIPS instruction format
| Name | Fields | Comments |
| Field size | 6 bits| 5 bits| 5 bits| 5 bits| 5 bits| 6 bits| All MIPS instructions 32 bits |
| R-format | op | rs | rt | rd |shamt| funct | Arithmetic instruction format |
| I-format | op | rs | rt | address/immediate | Transfer,branch,imm. format |
| J-format | op | target address | Jump instruction format |
MIPS operands
| Name | Example |
| 32 registers | $s0~$s7, $t0~$t9,$zero, $a0~$a3, $v0~$v1, $gp $fp, $gp, $ra, $at |
| Mem words | Memory[0], Memory[4], . . . , Memory[4294967292] |
MIPS assembly language
  ALU
    add add $s1, $s2, $s3
    subtract sub $s1, $s2, $s3
    add immediate addi $s1, $s2, -3 (Note: subi does not exist)

## Slide 19
  Data transfer
    load word lw $s1, 100($s2)
    store word sw $s1, 100($s2)
    load byte lb $s1, 100($s2)
    store byte sb $s1, 100($s2)
    load upper immediate lui $s1, 100
  Conditional branch
    branch on equal beq $s1, $s2, 25
    branch on not equal bne $s1, $s2, 25
    set on less than slt $s1, $s2, $s3
    set on less than immediate slti $s1, $s2, 100
  Unconditional jump
    jump j 2500
    jump register jr $ra
    jump and link jal 2500

## Slide 20: Tips on Assembler
Principle：
  It’s not requisite to obey the conventions
Example
  Jump back from procedure instead of using Jr ra
  Jump into or out of a procedure directly.
What could you do if there are more than 4 parameters for the procedure?
Push the parameters into the stack before Jal and then pop it out in the procedure.
Use free register to transfer the parameter

## Slide 21: Compilers & the SPIM Simulator
SPIM is a simulator that reads in an assembly program
and models its behavior on a MIPS processor
Note that a “MIPS add instruction” will eventually be
converted to an add instruction for the host computer’s
architecture – this translation happens under the hood
To simplify the programmer’s task, it accepts
pseudo-instructions, large constants, constants in
decimal/hex formats, labels, etc.
The simulator allows us to inspect register/memory
values to confirm that our program is behaving correctly

## Slide 22
Example
This simple program (similar to what we’ve written in class) will run
on SPIM (a “main” label is introduced so SPIM knows where to start)
main:
addi $t0, $zero, 5
addi $t1, $zero, 7
add $t2, $t0, $t1
If we inspect the contents of $t2, we’ll find the number 12

## Slide 23
User Interface
main:
addi $t0, $zero, 5
addi $t1, $zero, 7
add $t2, $t0, $t1
File add.s
rajeev@trust > spim
(spim) read “add.s”
(spim) run
(spim) print $10
Reg 10 = 0x0000000c (12)
(spim) reinitialize
(spim) read “add.s”
(spim) step
(spim) print $8
Reg 8 = 0x00000005 (5)
(spim) print $9
Reg 9 = 0x00000000 (0)
(spim) step
(spim) print $9
Reg 9 = 0x00000007 (7)
(spim) exit

## Slide 24
Directives
.text
.globl main
main:
addi $t0, $zero, 5
addi $t1, $zero, 7
add $t2, $t0, $t1
…
jal swap_proc
jr $ra
.globl swap_proc
swap_proc:
…
File add.s
Stack
Dynamic data (heap)
Static data (globals)
Text (instructions)
This function is visible to other files

## Slide 25
Directives
.data
.word 5
.word 7
.byte 25
.asciiz “the answer is”
.text
.globl main
main:
lw $t0, 0($gp)
lw $t1, 4($gp)
add $t2, $t0, $t1
…
jal swap_proc
jr $ra
File add.s
Stack
Dynamic data (heap)
Static data (globals)
Text (instructions)

## Slide 26
Labels
.data
in1 .word 5
in2 .word 7
c1 .byte 25
str .asciiz “the answer is”
.text
.globl main
main:
lw $t0, in1
lw $t1, in2
add $t2, $t0, $t1
…
jal swap_proc
jr $ra
File add.s
Stack
Dynamic data (heap)
Static data (globals)
Text (instructions)

## Slide 27
Endian-ness
Two major formats for transferring values between registers and memory
Memory: low address 45 7b 87 7f high address
Little-endian register: the first byte read goes in the low end of the register
Register: 7f 87 7b 45
Most-significant bit Least-significant bit
Big-endian register: the first byte read goes in the big end of the register
Register: 45 7b 87 7f
Most-significant bit Least-significant bit

## Slide 28
System Calls
SPIM provides some OS services: most useful are
operations for I/O: read, write, file open, file close
The arguments for the syscall are placed in $a0-$a3
The type of syscall is identified by placing the appropriate
number in $v0 ( li $v0, 1–10), “1-10” means one of the
OS service ID number
for example: 1 for print_int, 4 for print_string, 5 for read_int
$v0 is also used for the syscall’s return value

## Slide 29: System call

## Slide 30
Example Print Routine
.data
str: .asciiz “the answer is ”
.text
li $v0, 4 # load immediate; 4 is the code for print_string
la $a0, str # the print_string syscall expects the string
# address as the argument; la is the instruction
# to load the address of the operand (str)
syscall # SPIM will now invoke syscall-4
li $v0, 1 # syscall-1 corresponds to print_int
li $a0, 5 # print_int expects the integer as its argument
syscall # SPIM will now invoke syscall-1

## Slide 31
Example
Write an assembly program to prompt the user for two numbers and
print the sum of the two numbers

## Slide 32
Answer for Example
.text .data
.globl main str1: .asciiz “Enter 2 numbers:”
main: str2: .asciiz “The sum is ”
li $v0, 4
la $a0, str1
syscall # print str1 on screen
li $v0, 5
syscall # read in 1st integer
add $t0, $v0, $zero # $t0  1st input integer
li $v0, 5
syscall # read in 2nd integer
add $t1, $v0, $zero # $t1  2nd input integer
li $v0, 4
la $a0, str2
syscall # print str2 on screen
li $v0, 1
add $a0, $t1, $t0
syscall # print $t0+$t1 on screen

## Slide 33
2.12 Translating and starting a Program
C Program
Assembly language program
Object: machine language module
Object: library routine (machine language)
Executable: machine language program
Memory
Compiler
Assembler
Linker
Loader
x.c
x.s
x.o
x.a, x.so
a.out
A translation hierarchy

## Slide 34
Role of Assembler
Convert pseudo-instructions into actual hardware
instructions – pseudo-instrs make it easier to program
in assembly – examples: “move”, “blt”, 32-bit immediate
operands, etc.
Convert assembly instructions into machine instructions
  a separate object file (x.o) is created for each C file (x.c)
  compute the actual values for instruction labels
  maintain info on external references and debugging information

## Slide 35
Role of Linker
Stitches different object files into a single executable
  patch internal and external references
  determine addresses of data and instruction labels
  organize code and data modules in memory
Some libraries (DLLs) are dynamically linked – the
executable points to dummy routines – these dummy
routines call the dynamic linker-loader so they can
update the executable to jump to the correct routine

## Slide 36
Compilation Steps
The front-end: deals mostly with language specific actions
  Scanning: reads characters and breaks them into tokens
  Parsing: checks syntax
  Semantic analysis: makes sure operations/types are
  meaningful
  Intermediate representation: simple instructions,
  infinite registers, makes few assumptions about hw
The back-end: optimizations and code generation
  Local optimizations: within a basic block
  Global optimizations: across basic blocks
  Register allocation

## Slide 37
Compiler: Dataflow
Control flow graph: each box represents a basic block and
arcs represent potential jumps between instructions
For each block, the compiler computes values that were
defined (written to) and used (read from)
Such dataflow analysis is key to several optimizations:
for example, moving code around, eliminating dead code,
removing redundant computations, etc.

## Slide 38
Compiler: Register Allocation
The IR contains infinite virtual registers – these must be mapped to
the architecture’s finite set of registers (say, 32 registers)
For each virtual register, its live range is computed (the range
between which the register is defined and used)
We must now assign one of 32 colors to each virtual register so that
intersecting live ranges are colored differently – can be mapped to the
famous graph coloring problem
If this is not possible, some values will have to be temporarily spilled
to memory and restored (this is equivalent to breaking a single live
range into smaller live ranges)

## Slide 39
Compiler: High-Level Optimizations
High-level optimizations are usually hardware independent
Procedure inlining
Loop unrolling
Loop interchange, blocking (more on this later when we
study cache/memory organization)

## Slide 40
Compiler: Low-Level Optimizations
Common sub-expression elimination
Constant propagation
Copy propagation
Dead store/code elimination
Code motion
Induction variable elimination
Strength reduction
Pipeline scheduling

## Slide 41: Start a C program in a file on disk to run
Compiling
  C program  assembly language program
Assembling
  Assembly language program  machine language module
  pseudoinstructions
    move $t0,$t1 # register St0 gets register $t1
    add $t0,$zero, $t1 # register St0 gets 0+register $t1
  Symbol table
    A table that matches name of lables to the addresses of the memory words that instructions occupy.
object file

## Slide 42: Object file of UNIX (six distinct pieces)
object file header—size and position of the other pieces
Text segment
static data segment and dynamic data
The relocation information ----identifies absolute addresses of instruction and data words when the program is loaded into memory
Symbol table
Debugging information
Object file header |  |  | 
 | Name | Procedure A | 
 | Text size | 100hex | 
 | Data size | 20hex | 
Text segment | Address | instruction | 
 | 0 | lw $a0, 0($gp) | 
 | 4 | jal 0 | 
 | …… | -- | 
Data segment | 0 | (X) | 
 | …… | …… | 
Relocation information | Address | Instruction type | Dependency
 | 0 | Lw | X
 | 4 | jal | B
Symbol table | label | Address | 
 | X | -- | 
 | B | -- | 

## Slide 43: Linking
  Object modules(including library routine)  executable program
  3 step of Link
    Place code and data modules symbolically in memory
    Determine the addresses of data and instruction labels
    Patch both the internal and external references (Address of invoke)
0
$sp
7fff fffchex
$gp
1000 8000hex
PC
0040 0000hex
Dynamic data
Stack
Static data
Reserved
Text
1000 0000hex
Link object file A & B
0000000000000000 0111111111111111 + 215
0001000000000000 1000000000000000
1111111111111111 1000000000000000 -215
+
0001000000000000 0000000000000000

## Slide 44: Loading
  Determine size of text and data segments
  Create an address space large enough
  Copy instructions and data from executable file to memory
  Copy parameters (if any) to the main program onto the stack
  Initialize registers and set $sp to the first free location
  Jump to a start-up routine

## Slide 45: 2.13 A C Sort Example to Put it All Together
3 steps for translating C procedures
  Allocate registers to program variables
  Produce code for the body of the procedures
  Preserve registers across the procedures invocation

## Slide 46
Procedure swap (C code)
  swap ( int v[ ] , int k )
  {
  int temp ;
  temp = v[ k ] ;
  v[ k ] = v[ k + 1 ] ;
  v[ k + 1 ] = temp ;
  }

## Slide 47
The swap Procedure swap (v, j);
Register allocation:
  $a0 and $a1 for the two arguments,
  $t0 for the temp variable – no need for saves and restore
  this is a leaf procedure (won’t need to reuse $a0 and $a1)
swap: sll $t1, $a1, 2 ;$t1j*4
add $t1, $a0, $t1 ;$t1v[j] address = v + j*4
lw $t0, 0($t1) ; $t0 v[j]
lw $t2, 4($t1) ; $t2 v[j+1]
sw $t2, 0($t1) ; v[j]  $t2
sw $t0, 4($t1) ; v[j+1] $t0
jr $ra
Why use $a0, $a1 for V and j ?

## Slide 48
Full Example – Sort in C
void sort (int v[], int n)
{
int i, j;
for (i=0; i<n; i+=1) {
for (j=i-1; j>=0 && v[j] > v[j+1]; j-=1) {
swap (v,j);
}
}
}
void swap (int v[], int k)
{
int temp;
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}
V[0]
V[1]
V[2]
……
V[n-1]
If V[0]> V[1]

## Slide 49: Procedure sort
  C code
  sort ( int v[ ] , int n )
  {
  int i , j ;
  for ( i = 0 ; i < n ; i + = 1 ) {
  for ( j = i - 1 ; j >= 0 && v[j] > v[j+1] ; j- = 1 )
  swap ( v , j ) ;
  }
  }
  Register allocation for sort
  v ---- $a0 n ---- $a1 i ---- $s0 j ---- $s1
  Passing parameters in sort
  Preserving registers in sort
  $ra , $s0, $s1, $s2, $s3
V[0]
V[1]
V[2]
……
V[n-1]
If V[0]> V[1]

## Slide 50: Code for the procedure sort
  Saving registers
  sort: addi $sp, $sp, -20 # make room on stack for 5 registers
  sw $ra, 16($sp) # save $ra on stack
  sw $s3, 12($sp) # save $s3 on stack
  sw $s2, 8($sp) # save $s2 on stack
  sw $s1, 4($sp) # save $s1 on stack
  sw $s0, 0($sp) # save $s0 on stack
    Procedure body{Outer loop {Inner loop} }
    Restoring registers
    exit1: lw $s0, 0($sp) # restore $s0 from stack
    lw $s1, 4($sp) # restore $s1 from stack
    lw $s2, 8($sp) # restore $s2 from stack
    lw $s3, 12($sp) # restore $s3 from stack
    lw $ra, 16($sp) # restore $ra from stack
    addi $sp, $sp, 20 # restore stack pointer
    Procedure return
    jr $ra # return to calling routine

## Slide 51: Code for Procedure body
      Outer loop—first for loop
    for ( i = 0 ; i < n ; i + = 1 ) {
      Move parameters
      move $s2, $a0 # $s2 ← $a0 ($a0: base address, v)
      move $s3, $a1 # $s3 ← $a1 ($a1: array size, n )
      Outer loop
      move $s0, $zero # $s0 ← $zero ( i = 0)
  for1tst: slt $t0, $s0, $s3 # test if $s0 >= $s3 (i >= n)
      beq $t0, $zero, exit1 # go to exit1 if $s0 >= $s3 (i >= n)
      ………………
      （body of first for loop is second for loop）
      ………………
  exit2: addi $s0, $s0, 1 # i = i + 1
  j for1tst # jump to test of outer loop
  exit1:

## Slide 52: Inner loop--
      second for loop is body of first for loop
    addi $s1, $s0, -1 # j = i - 1
for2tst: slti $t0, $s1, 0 # test if j < 0
    bne $t0, $zero, exit2 # go to exit2 if j < 0
    sll $t1, $s1, 2 # $t1 = j * 4
    add $t2, $s2, $t1 # $t2 = the address of v[j]
    lw $t3, 0($t2) # $t3 = v[j]
    lw $t4, 4($t2) # $t4 = v[j + 1]
    slt $t0, $t4, $t3 # test if v[j+1]>=v[j]
    beq $t0, $zero, exit2 # go to exit2 if v[j+1]>=v[j]
      ………………
      （body of first for loop ）
    ………………
    addi $s1, $s1, -1 # j = j - 1
    j for2tst # jump to test of inner loop
  exit2:
  sort ( int v[ ] , int n )
  {
  int i , j ;
  for ( i = 0 ; i < n ; i + = 1 ) {
  for ( j = i - 1 ;
  j >= 0 && v[j] > v[j+1] ;
  j- = 1 )
  swap ( v , j ) ;
  }
  }

## Slide 53
      body of first for loop
      Pass parameters and call
    move $a0，$s2 # $a0←$s2 ($s2 : v )
    move $a1，$s1 # $a1←$s1 ($a1← j)
      Call function swap(int v[], int k)
    jal swap # ($a0 might be changed in swap)
Notice: 1.Why are $a0 and $a1 saved? $a0 is the base of the array v. $a0 will be used repeatedly and might be(actually not here) changed by the procedure swap. $a1 is the size of the array v. $a1 will be used repeatedly and changed before the procedure swap is called.
2.Why are they not pushed to stack?
  Register variable is faster

## Slide 54
Relative Performance
Gcc optimization Relative Cycles Instruction CPI
performance count
none 1.00 159B 115B 1.38
O1 2.37 67B 37B 1.79
O2 2.38 67B 40B 1.66
O3 2.41 66B 45B 1.46
A Java interpreter has relative performance of 0.12, while the
Jave just-in-time compiler has relative performance of 2.13
Note that the quicksort algorithm is about three orders of
magnitude faster than the bubble sort algorithm (for 100K elements)

## Slide 55: 2.14 Arrays versus Pointers
Array version
  clear1 ( int array[ ], int size )
  {
  int i;
  for ( i = 0 ; i < size ; i = i + 1 )
  array[i] = 0;
  }
Pointer version
    clear2 ( int *array, int size )
    {
    int *p;
    for ( p = &array[0] ; p < &array[size] ; p = p + 1 )
    *p = 0;
    }

## Slide 56: Assembly code(array version)
Assembly code for clear-1 procedure
  move $t0, $zero # i = 0
  loop1: sll $t1, $t0, 2 # $t1 = i * 4
  add $t2, $a0, $t1 # $t2 = address of array[ i ]
  sw $zero, 0($t2) # array[ i ] = 0
  addi $t0, $t0, 1 # i = i +1
  slt $t3, $t0, $a1 # test if i < size
  bne $t3, $zero, loop1 # if ( i < size ) go to loop1
  jr $ra
  This code works as long as size is greater than 0. (In this case, the loop will be executed once even though the value of the size parameter is invalid. Actually, size >0 must be checked at first)

## Slide 57: Assembly code ( pointer version)
Assembly code for clear-2 procedure
  move $t0, $a0 # p = the start address of the array[]
  sll $t1, $t1, 2 # $t1 = size * 4
  add $t2, $a0, $t1 # $t2 = &array[size](address of array[size] )
  loop2: sw $zero, 0($t0) # Memory[ p ] = 0
  addi $t0, $t0, 4 # p = p + 4
  slt $t3, $t0, $t2 # $t3 = (p < &array[size] )
  bne $t3, $zero, loop2 # if ( p < &array[size] ) go to loop2
  jr $ra
  This code works as long as size is greater than 0.
Compare the two versions
  Array version has the “multiply” and add inside loop
  Pointer version reduces instructions/iteration from 6 to 4
For modern compliers, both ways are the same.

## Slide 58: 2.16 Real Stuff: IA-32 Instructions
The Intel IA-32
  1978 intel 8086
    16-bit architecture
    Is not considered a general-purpose register
  1980 intel 8087 floating-point coprocessor
  1982 80286 extended the 8086 architecture by
    Increasing Address Space to 24 bits
    Manipulate the protection model
  1985 80386 extended the 80286 architecture
    32-bit architecture with 32-bit registers
    32-bit address space
    Add paging support in addition to segmented addressing
    Nearly a general-purpose register machine ?

## Slide 59
  1989~95 Higher performance
    80486 in 1989
    Pentium in 1992
    Pentium Pro in 1995
  1997 Expand Pentium and Pentium Pro with MMX
  1999 Expand Pentium with SSE(SIMD) as Pentium III
    8 separate registers ,double their width to 128 bits
    Add a single-precision floating-point data type
    4 32-bit floating-point operations can be performed in parallel
    Cache prefetch instructions
  2001 Intel Pentium 4
  2003 A company other than Intel enhanced the IA-32 architecture
    AMD
    Executing all IA-32 instructions with 64-bit Address space & data
  2004 Intel capitulates and embraces AMD64

## Slide 60
80x86 registers and data addressing modes
    80386 extended all 16-bit registers but segment ones to 32 bits
    GPR ( general-purpose register )
    Addressing modes
      Register indirect
      Based mode with 8- or 32-bit displacement
      Base plus scaled index
      Base plus scaled index with 8- or 32-bit displacement
80x86 integer operations
    Data movement instructions
    Arithmetic and logic instructions
    Control flow
    String instructions

## Slide 61: IA-32 Register and Data Addressing Modes
Name | Register no. | Usage
$zero | 0 | The constant value 0
$v0-$v1 | 2-3 | Values for results and expression evaluation
$a0-$a3 | 4-7 | Arguments
$t0-$t7 | 8-15 | Temporaries
$s0-$s7 | 16-23 | Saved
$t8-$t9 | 24-25 | More temporaries
$gp | 28 | Global pointer
$sp | 29 | Stack pointer
$fp | 30 | Framer pointer
$ra | 31 | Return address

## Slide 62: Instruction types for ALU & data transfer
Source/destination operand type | Second source operand
Register | Register
Register | Immediate
Register | Memory
Memory | Register
Memory | Immediate

## Slide 63: Some typical IA-32 Integer Operations

## Slide 64: Typical 80x86 instruction format
1Byte
5Bytes
3Bytes
1Bytes
5Bytes
6Bytes

## Slide 65: 2.18 Concluding Remarks
Two principles of stored-program computers
  Use instructions as numbers
  Use alterable memory for programs
Four design principles
  Simplicity favors regularity
  Smaller is faster
  Make the common case fast
  Good design demands good compromises
MIPS instruction set

## Slide 66: 2.19 History of Instruction Set Development
Accumulator Architectures
  Only 1 register for arithmetic instructions: accumulator
  Memory-based operand-addressing mode
Example 2.23 Compiling C code to accumulator instructions
  C code: A = B + C ;
  Accumulator instructions:
    load AddressB # Acc = Memory[AddressB], or Acc = B
    add AddressC # Acc = Acc + Memory[AddressC], or Acc = B + C
    store AddressA # Memory[AddressA] = Acc, or A = B + C
Extended Accumulator Architectures

## Slide 67: General-Purpose Register Architectures
  Register-memory architecture
    80386
    IBM 360
  Load-store or register-register architecture
    CDC 6600
    MIPS
  DEC’s VAX architecture
    Allow any combination of registers and memory operands
    Memory-memory architecture
Example 2.24 Compiling C code to memory-memory instructions
  C code: A = B + C;
  instructions:
    add AddressA, AddressB, AddressC

## Slide 68: Compact Code and Stack Architectures
  Variable-length instructions
    To match the varying operand specifications
    To minimize code size
  Stack model of execution
    All registers are abandoned,so the instructions are short.
    Push, pop
Example 2.25 Compiling C code to stack instructions
  C code: A = B + C;
  Stack instructions:
    push AddressC # Top = Top+4; Stack[Top]=Memory[AddressC]
    push AddressB # Top = Top+4; Stack[Top]=Memory[AddressB]
    add # Stack[Top-4]= Stack[Top]+Stack[Top-4];Top=Top-4;
    pop AddressA # Memoryp[AddressA]=Stack[Top]; Top=Top-4;

## Slide 69
High-Level-Language Computer Architecture
  Goal: hardware more like programming languages
  Finally failed
Reduced Instruction Set Computer Architecture (RISC )
  Fixed instruction lengths
  Load-store instruction sets
  Limited addressing modes
  Limited operations
  MIPS, Sun SPARC, Hewlett-Packard PA-RISC
  IBM PowerPC, DEC Alpha

## Slide 70: Static data segment
全局区（静态区）
  全局变量和静态变量的存储是放在一块的
  初始化的全局变量和静态变量在一块区域
  未初始化的全局变量和未初始化的静态变量在相邻的另一块区域
  程序结束后有系统释放
文字常量区
  常量字符串就是放在这里的。
  程序结束后由系统释放

## Slide 71: TEXT segment
代码段
程序代码区—存放函数体的二进制代码

## Slide 72: Segment fault（segfault）
Run out of memory
  Heap指针遇到stack指针
越界访问内存
non-existent address
a buffer overflow
using uninitialized pointers
…

## Slide 73: variable
#define PI 3
  PI不是变量，不能取地址，不能赋值
  PI是一个符号
  汇编中直接用数值
Const int PI=3
  PI是变量，能取地址，不能赋值
  PI是一个符号，等同于变量地址
  汇编中直接用变量地址
int PI=3; 或者 auto int PI=3;
  PI是变量，能取地址，能赋值
  PI是一个符号，等同于变量地址
  汇编中直接用变量地址
Registor int PI=3
  PI是变量，在寄存器中不能取地址，能赋值
  PI是一个符号，等同于寄存器号
  汇编中直接用寄存器号
PI存储在符号表中，无存储空间
从高级语言翻译到汇编时直接替代
PI有存储空间，在内存的数据段中，静态分配
在符号表中是常量变量，指向存储空间，不能修改值
PI有存储空间，在内存的栈中
随着PI所在函数进入运行，动态分配，从栈中指定一个空间给PI变量
在符号表中是常量变量，指向存储空间
PI无存储空间，直接在寄存器
在符号表中是寄存器变量，指向寄存器