## Slide 1: Computer Organization & Design —The Hardware/ Software Interface
Chapt3_1

## Slide 2: Contents
3.1 Introduction
3.2 Signed and Unsigned Numbers-Possible Representations
3.3 Arithmetic--Addition & subtraction and ALU
3.4 Multiplication
3.5 Division
3.6 Floating point numbers

## Slide 3: 3.1 Introduction
Computer words are composed of bits; thus words can be represented as binary numbers.
Simplified to contain only:
  memory-reference instructions: lw, sw
  arithmetic-logical instructions: add, sub, and, or, slt
  control flow instructions: beq, j
Generic Implementation:
  use the program counter (PC) to supply instruction address
  get the instruction from memory
  read registers
  use the instruction to decide exactly what to do
All instructions use the ALU after reading the registers Why? memory-reference? arithmetic? control flow?

## Slide 4: 3.1 Introduction
Computer words are composed of bits; thus words can be represented as binary numbers.
What about fractions and other real numbers?
What happen if an operations creates a number bigger than can be represented
And underlying these questions is a mystery: How does hardware really multiply or divide numbers?

## Slide 5: Numbers
Bits are just bits (no inherent meaning)— conventions define relationship between bits and numbers
Binary numbers (base 2) 0000 0001 0010 0011 0100 0101 0110 0111 1000 1001... decimal: 0...2n-1
Of course it gets more complicated: numbers are finite (overflow) fractions and real numbers negative numbers e.g., no MIPS subi instruction; addi can add a negative number)
How does hardware really multiply or divide numbers?

## Slide 6: 3.2 Signed and Unsigned Numbers Possible Representations
Sign Magnitude: One's Complement Two's Complement 000 = +0 000 = +0 000 = +0 001 = +1 001 = +1 001 = +1 010 = +2 010 = +2 010 = +2 011 = +3 011 = +3 011 = +3 100 = -0 100 = -3 100 = -4 101 = -1 101 = -2 101 = -3 110 = -2 110 = -1 110 = -2 111 = -3 111 = -0 111 = -1
Issues: number of zeros, ease of operations
Which one is best? Why?

## Slide 7: Numbers and their representation
Number systems
  Radix based systems are dominating
  decimal, octal, binary,…
  b: value of the digit, k: radix, n: digits left of radix point, m: digits right of radix point
  Alternatives, e.g. Roman numbers (or Letter)
Decimal (k=10) -- used by humans
Binary (k=2) -- used by computers
0≤b≤K
(N)k＝(An－1A n－2A n－3…A 1A 0 • A-1A -２A…A –m+1A – m)k
MSB
LSB

## Slide 8: Numbers and their representation
Representation
  ASCII - text characters
    Easy read and write of numbers
    Complex arithmetic (character wise)
  Binary number
    Natural form for computers
    Requires formatting routines for I/O

## Slide 9: Endianness/byte order
Big end：Leftmost
  Mips，powerpc
  01 02 = 258
Little end：Rightmost
  X86， ARM
  01 02 = 513
Bi-endian
  ARM，PowerPC, Alpha, SPARC

## Slide 10: Signed number representation
First idea:
  Positive and negative numbers
  Take one bit (e.g. 31) as the sign bit
    Problem
    0 0000000 = 0 positive zero!
    1 0000000 = 0 negative zero!
  Each comparison to 0 requires two steps
1's complement
2's complement

## Slide 11: Number types
Integer numbers, unsigned
  Address calculations
  Numbers that can only be positive
Signed numbers
  Positive
  Negative
Floating point numbers
  numeric calculations
  Different grades of precision
    Singe precision (IEEE)
    Double precision (IEEE)
    Quadruple precision

## Slide 12: Number formats
Sign and magnitude
2's complement
1's complement
similar to 2's complement, + 0 & - 0
Biased notation
1000 0000 = minimal negative value(-27)
0111 1111 = maximal positive value (27-1)
Representation
  Binary
  Decimal
  Hexadecimal

## Slide 13: Two's Complement Operations
Negating a two's complement number:
invert all bits and add 1 with end
  remember: “negate” and “invert” are quite different!
Defining : Assume:x＝±0.x-1x-２x-３…x-m OR x＝±xn－1xn－２xn－３xn－4…x0
Converting n bit numbers into numbers with more than n bits:
  MIPS 16 bit immediate gets converted to 32 bits for arithmetic
  copy the most significant bit (the sign bit) into the other bits 0010 -> 0000 0010 1010 -> 1111 1010
Ｘ 0≤X<1
２＋Ｘ＝2－|Ｘ| -1≤X<0
Ｘ 0≤X<2n
2n+1＋Ｘ＝2n+1－|Ｘ| -2n≤X<0
fraction
integer
[X]C＝

## Slide 14: 2's complement for n=3
Only one representation for 0
All numbers less than zero has the MSB = 1
One more negative number than positive number
2n+1＋Ｘ＝2n+1-|Ｘ|
＝ 24 －8
＝(10000-1000)2
＝ 01000
Ex2: 37: 0 0 1 0 0 1 0 1
1 1 0 1 1 0 1 0
1 1 1 1 1 1 1 1
+ 1  1101 1011 (-37)
0 0 0 0 0 0 0 0

## Slide 15: If x<0, how to know its IxI ?
Ex2: -37: 1 1 0 1 1 0 1 1
0 0 1 00 1 0 0
1 1 1 1 1 1 1 1
+ 1  00100101 (37)
0 0 0 0 0 0 0 0

## Slide 16: Why use 2’s complement ? -----natural way to present
Ex1: one sign bit 1’s comlement 2’s complement
  +5 0 1 0 1 0 1 0 1 0101
  -5 1 1 0 1 1 0 1 0 1011
  0 0 0 1 0(2) 1 1 1 1 (-0) 0000 (good)
Problem for 1’s complement
  0001 0011 19
  − 1111 1100 −3
  1 0001 0111 23 —An end-around borrow is produced.
  − 0000 0001 1 —Subtract end-around borrow from result.
  0001 0110 22 —The correct result (19 − (−3) = 22).

## Slide 17: Another good thing for 2’s complement
We don’t need subtraction
EX:
1’s complement 2’s complement
  ------------------------- --------------------------
  0001 0011 19 0001 0011 19
  − 1111 1100 −3 + 1111 1101 -3
  1 0001 0111 23 1 0001 0000 16
  − 0000 0001 1
  0001 0110 22

## Slide 18: More common: use of 2's complement---- negatives have one additional number
(0000 0000 0000 0000 0000 0000 0000 0000)2 =(0)10
(0000 0000 0000 0000 0000 0000 0000 0001)2 =(1)10
………… ………
(0111 1111 1111 1111 1111 1111 1111 1101)2 =( 2，147，483，645)10
(0111 1111 1111 1111 1111 1111 1111 1110)2 =( 2，147，483，646)10
(0111 1111 1111 1111 1111 1111 1111 1111)2 =( 2，147，483，647)10
(1000 0000 0000 0000 0000 0000 0000 0000)2 =(-2，147，483，648)10
(1000 0000 0000 0000 0000 0000 0000 0001)2 =(-2，147，483，647)10
(1000 0000 0000 0000 0000 0000 0000 0010)2 =(-2，147，483，646)10
………… ………
(1111 1111 1111 1111 1111 1111 1111 1101)2 =(-3)10
(1111 1111 1111 1111 1111 1111 1111 1110)2 =(-2)10
(1111 1111 1111 1111 1111 1111 1111 1111)2 =(-1)10

## Slide 19: sign extension (lbu vs. lb)
Sign Extension
e.g. 16 bit numbers to 32 bit numbers
Required for operations with registers(32 bits) and immediate operands (16 bits)
Sign extension
  Take the lower 16 bits as they are
  Copy the highest bit to the remaining 16 bits
  0000 0000 0000 0010 → 2
  0000 0000 0000 0000 0000 0000 0000 0010
  1111 1111 1111 1110 → -2
  1111 1111 1111 1111 1111 1111 1111 1110

## Slide 20: Compare operations
Different compare operations required for both number types
  Signed integer
    slt Set when less than
    slti Set when less than immediate
  Unsigned integer
    sltu Set when less than
    sltiu Set when less than immediate

## Slide 21: Example for Compare
Register $s0
1111 1111 1111 1111 1111 1111 1111 1111
Register $s1
0000 0000 0000 0000 0000 0000 0000 0001
Compared Operations
slt $t0, $s0, $s1
sltu $t0, $s0, $s1
Results
$t0 = 1 (-1 < 1)
$t0 = 0 (4,294,967,295ten > 1ten)

## Slide 22: Effects of Overflow
An exception (interrupt) occurs
  Control jumps to predefined address for exception
  Interrupted address is saved for possible resumption
Don't always want to detect overflow — new MIPS instructions: addu, addiu, subu
note: addiu still sign-extends! note: sltu, sltiu for unsigned comparisons

## Slide 23: 3.3 Arithmetic
Addition and Subtraction
Logical operations
Constructing a simple ALU
Multiplication
Division
Floating point arithmetic
Adding all parts to get an ALU

## Slide 24: Addition & subtraction
Adding bit by bit, carries -> next digit
Subtraction
  Directly
  Addition of 2's complement

## Slide 25: Overflow
The sum of two numbers can exceed any representation
The difference of two numbers can exceed any representation
2's complement:
Numbers change
sign and size

## Slide 26: Overflow conditions
General overflow conditions
Reaction on overflow
  Ignore ?
  Reaction of the OS
  Signaling to application (Ada, Fortran,...)

## Slide 27: Overflow process
Hardware detection in the ALU
Generation of an exception (interrupt)
Save the instruction address (not PC) in special register EPC
Jump to specific routine in OS
  Correct & return to program
  Return to program with error code
  Abort program

## Slide 28: Which instructions cause Overflow
Overflows in signed arithmetic instructions cause exceptions:
  add
  add immediate (addi)
  subtract (sub)
Overflows in unsigned arithmetic instructions don’t cause exceptions
  add unsigned (addu)
  add immediate unsigned (addiu)
  Subtract unsigned (subu)
Handle with care!

## Slide 29: New MIPS instructions
Byte instructions
  lbu: load byte unsigned
    Loads a byte into the lowest 8 bit of a register
    Fills the remaining bits with '0'
  Lb: load byte (signed)
    Loads a byte into the lowest 8 bit of a register
    Extends the highest bit into the remaining 24 bits
Set instructions for conditional branches
  sltu: set on less than unsigned
  sltiu: set on less than unsigned immediate

## Slide 30: Logical operations
Logical shift operations
  right (srl)
  left (sll)
The machine instruction for the instruction sll $t2, $s0, 3 (sll rd, rt, i)
Example: sll $t2, $s0, 3
  $s0: 0000 0000 0000 0000 1100 1000 0000 1111
  $t2: 0000 0000 0000 0110 0100 0000 0111 1000
Op | Rs | Rt | Rd | Shamt | Adr/funct
0 | 0 | 16 | 10 | 3 | 0
Filled with '0'

## Slide 31: Logical operations
AND→bit-wise AND between registers
and register1, register2, register3
OR →bit-wise OR between registers
or register1, register2, register3
Example:
and $3, $10, $16
or $4, $10, $16
  R16: 0000 0000 0000 0000 1100 1000 0000 1111
  R10: 0000 0000 0000 0110 0100 0000 0111 1000
  R3: 0000 0000 0000 0000 0100 0000 0000 1000
  R4: 0000 0000 0000 0110 1100 1000 0111 1111

## Slide 32: Constructing an ALU
Step by step: build a single bit ALU and expand it to the desired width
First function: logic AND and OR

## Slide 33: A half adder
Sum = a b + a b
Carry = a b

## Slide 34: A full adder
Accepts a carry in
Sum = A xor B xor CarryIn
CarryOut = B CarryIn + A CarryIn + A B
Inputs |  |  | Outputs |  | Comments (two)
A | B | CarryIn | CarryOut | Sum | 
0 | 0 | 0 | 0 | 0 | 0+0+0=00
0 | 0 | 1 | 0 | 1 | 0+0+1=01
0 | 1 | 0 | 0 | 1 | 0+1+0=01
0 | 1 | 1 | 1 | 0 | 0+1+1=10
1 | 0 | 0 | 0 | 1 | 1+0+0=01
1 | 0 | 1 | 1 | 0 | 1+0+1=10
1 | 1 | 0 | 1 | 0 | 1+1+0=10
1 | 1 | 1 | 1 | 1 | 1+1+1=11

## Slide 35: Full adder
Full adder in 2-level design

## Slide 36: 1 bit ALU
ALU
  AND
  OR
  ADD
Cascade Element

## Slide 37: Basic 32 bit ALU
Inputs parallel
Carry is cascaded
Ripple carry adder
行波进位加法器
Slow, but simple
1st Carry In = 0

## Slide 38: Extended 1 bit ALU
Subtraction
a - b
  a-b = a + (~b+1)
  =a + (-b)
  Inverting b
  1st CarryIn= 1

## Slide 39: Extended 1 bit ALU with NOR
NOR
~(a+b) = ~a · ~b
Inverting A
Using the same and gate.
ALU
  Add
  And, Or, Nor
  Sub

## Slide 40: Extended 1 bit ALU to MIPS ALU
Functions
  AND
  OR
  Add
  Subtract
Missing: comparison
  Slt rd, rs, rt
  If rs < rt, rd=1, else rd=0
  All bits = 0 except the least significant
  Subtraction (rs - rt), if the result is negative -> rs < rt
  Use of sign bit as indicator

## Slide 41: Extended 1 bit ALU
ALU bit with input for Less data

## Slide 42: Most significant bit
Set for comparison
Overflow detect

## Slide 43: Complete ALU
Input
  A
  B
Control lines
  Operation
  Binvert
  Carryin
Output
  Result
  Overflow

## Slide 44: Complete ALU
Add a Zero detector

## Slide 45: ALU symbol & control
Function table
Symbol of the ALU
ALU Control Lines | Function
000 | And
001 | Or
010 | Add
110 | Sub
111 | Set on less than

## Slide 46: Speed considerations
Previously used: ripple carry adder
Delay for the sum: two units
Delay for the carry: two - three units

## Slide 47: Speed considerations
Delay of one adder
  2 time units
Total delay for
stages:
2n unit delays
Not appropriate for
high speed application

## Slide 48: Fast adders
All functions can be represented in 2-level logic.
But:
  The number of inputs of the gates would drastically rise
Target:
Optimum between speed and size

## Slide 49: Fast adders
Carry look-ahead adder
  Calculating the carries before the sum is ready
Carry skip adder（进位跳跃加法器）
  Accelerating the carry calculation by skipping some blocks
Carry select adder（进位选择加法器）
  Calculate two results and use the correct one
...

## Slide 50: Carry look ahead adder (CLA)
Separation of
  add operation
  carry calculation
Factorization
  Ci+1 = (bi * ci) + (ai * ci) + (ai * bi)
  =(ai * bi) + (ai + bi) * ci
  Generate gi = ai * bi
  Propagate pi = ai + bi

## Slide 51: Carry Look Ahead adder(CLA) 超前进位加法器
Ci+1 = gi + pi * ci
Carry generate: gi = ai * bi
  If a and b are '1' ->
  we always have a carryout independent of ci
Carry propagate: pi = ai+ bi
  If only one of a and b is '1' ->
  the carry out depends on the carry in
  pi propagates the carry

## Slide 52: Four bit carry look ahead adder
c1 = g0 + (p0 * c0)
c2 = g1 + p1*c1 = g1 + (p1 * g0) + (p1 * p0 * c0)
c3 = g2 + p2*c2 = g2 + (p2 * g1) + (p2 * p1 * g0) + (p2 * p1 * p0 * c0)
c4 = g3 + p3*c3 = g3 + (p3 * g2) + (p3 * p2 * g1)
+(p3 * p2 * p1 * g0) + (p3 * p2 * p1 * p0 * c0)
COMMENT:
This kind of adder will be faster than the ripple carry adder, and smaller than the adder with the tow-level logic.
PROBLEM:
If the number of the adder bits is very large, then this kind of adder will be too large. So we must seek more efficient ways.

## Slide 53: Four bit carry look ahead adder
Let’s consider a 16-bit adder.
Divide 16 bits into 4 groups. Each group has 4 bits.
As we know:
c4 = g3 + p3*g2 + p3*p2*g1 + p3*p2*p1*g0 + p3*p2*p1*p0*c0
So,we can get the following:
c8 = g7 + p7*g6 + p7*p6*g5 + p7*p6*p5*g4 + p7*p6*5*p4*c4
c12 = g11+p11*g10+p11*p10*g9+p11*p10*p9*g8+p11*p10*p9*p8*c8
c16=g15+p15*g14+p15*p14*g13+p15*p14*p13*g12+p15*p14*p13*p12*c12
Assume: G0= g3 + p3*g2 + p3*p2 *g1 +p3*p2*p1*g0
G1= g7 + p7*g6 + p7*p6*g5 + p7*p6*p5*g4
G2= g11+p11*g10+p11*p10*g9+p11*p10*p9*g8
G3= g15+p15*g14+p15*p14*g13+p15*p14*p13*g12
P0= p3 * p2 * p1 * p0
P1= p7 * p6 * p5 * p4
P2= p11 * p10 * p9 * p8
P3= p15 * p14 * p13 * p12

## Slide 54: Four bit carry look ahead adder
Then we get:
c4=G0+P0*c0 ; c8=G1+P1*c4
c12=G2+P2*c8 ; c16=G3+P3*c12
Assume: C1=c4, C2=c8, C3=c12, C4=c16
Then:
C1=G0+P0*c0 ; C2=G1+P1*C1
C3=G2+P2*C2 ; C4=G3+P3*C3
And,we can further get:
C1=G0+P0*c0 ;
C2= G1+P1*C1 = G1+P1*G0+ P1* P0*c0
C3=G2+P2*C2 = G2+P2*G1 + P2* P1*G0+ P2* P1* P0*c0
C4=G3+P3*C3= G3+P3*G2+P3*P2*G1+P3*P2*P1*G0+P3*P2*P1*P0*c0

## Slide 55: Hybrid CLA + Ripple carry
Realisation:
  Ripple carry adders and
  Carry look ahead logic

## Slide 56: Carry-Skip Adders
With CMOS Implementation – Carry Skip Adder’s speed Comparable to CLA
Less Area/Power
Based on Observation that Carry Process Can “Skip” Stage for Which xi  yi (that is pi = xiyi = 1)
Adder of n stages Divided into Stages of Selected Lengths
With Simple Ripple Carry
Each Group Generates “Group Carry-Propagate”=1 if all pi=1 This Signal Allows Incoming Carry to “Skip” Stages within Group and Generate Carry-out

## Slide 57: What does it mean if ALL Pi = 1 ?
c1 = g0 + (p0 * c0)
c2 = g1 + p1*c1 = g1 + (p1 * g0) + (p1 * p0 * c0)
c3 = g2 + p2*c2 = g2 + (p2 * g1) + (p2 * p1 * g0) + (p2 * p1 * p0 * c0)
c4 = g3 + p3*c3 = g3 + (p3 * g2) + (p3 * p2 * g1)
+(p3 * p2 * p1 * g0) + (p3 * p2 * p1 * p0 * c0)
gi = ai * bi pi= ai + bi
If Pi = 1 then it can be know that Gi = 0
So, c4 = g3 + p3*c3 = g3 + (p3 * g2) + (p3 * p2 * g1)
+(p3 * p2 * p1 * g0) + (p3 * p2 * p1 * p0 * c0)
= c0

## Slide 58: Carry skip adder
Accelerating the carry by skipping the interior blocks
Optimal speed with no-equal distribution of block length

## Slide 59: Fixed Block Width Carry-Skip Adders

## Slide 60: Carry Select Adder (CSA)

## Slide 61: Carry Select Adder
Carry selection by nibbles

## Slide 62: 3.3 Multiplication
Binary multiplication
Multiplicand * Multiplier
1000 * 1001
1000
1001
1000
0000
0000
_1000_____
Product 1001000
Look at current bit position
  If multiplier is 1
    then add multiplicand
    Else add 0
  shift multiplicand left by 1 bit

## Slide 63: Multiplier V1
32 bits: multiplier
64 bits: multiplicand, product, ALU
0010*0011
6
4
-
b
i
t
A
L
U
C
o
n
t
r
o
l
t
e
s
t
M
u
l
t
i
p
l
i
e
r
S
h
i
f
t
r
i
g
h
t
P
r
o
d
u
c
t
W
r
i
t
e
M
u
l
t
i
p
l
i
c
a
n
d
S
h
i
f
t
l
e
f
t
6
4
b
i
t
s
6
4
b
i
t
s
3
2
b
i
t
s
0000 0110
0011
0000 0010

## Slide 64: Multiplier V 1
Requires 32 iterations
  Addition
  Shift
  Comparison
Almost 100 cycles
Very big, Too slow!

## Slide 65: Multiplier V 2
Real addition is performed only with 32 bits
Least significant bits of the product don't change
New idea:
  Don’t shift the multiplicand
  Instead,shift the product
  Shift the multiplier
ALU reduced to 32 bits!

## Slide 66: Multiplier V 2
Diagram of the V2 multiplier
Only left half of product register is changed

## Slide 67: Multiplier V 2
Addition performed
only on left half of
product register
Shift of product register

## Slide 68: Revised 4-bit example
Multiplicand x multiplier: 0001 x 0111
Multiplicand: 0001
Multiplier: 0111
00000000 #Initial value for the product
00010000 #After adding 0001
00001000 #After shifting right the product one bit
0001
00011000
00001100 #After shifting right the product one bit
0001
00011100
00001110 #After shifting right the product one bit
0000
00001110
00000111 #After shifting right the product one bit

## Slide 69: Multiplier V 3
Further optimization
At the initial state the product register contains only '0'
The lower 32 bits are simply shifted out
Idea:
use these lower 32 bits for the multiplier

## Slide 70: Multiplier V 3

## Slide 71: Multiplier V 3
Set product
register to '0'
Load lower
bits of product
register with
multiplier
Test least
significant bit
of product
register

## Slide 72: Example
Multiplicand x multiplier: 0001 x 0111
Multiplicand: 0001
Multiplier: 0111
00000111 #Initial value for the product
00010111 #After adding 0001
00001011 #After shifting right the product one bit
0001
00011011
00001101 #After shifting right the product one bit
0001
00011100
00001110 #After shifting right the product one bit
0000
00001110
00000111 #After shifting right the product one bit

## Slide 73: Signed multiplication
Basic approach:
  Store the signs of the operands
  Convert signed numbers to unsigned numbers
  (most significant bit (MSB) = 0)
  Perform multiplication
  If sign bits of operands are equal
  sign bit = 0, else
  sign bit = 1
Improved method:
Booth's Algorithm
Assumption: addition and subtraction are available

## Slide 74: Booth’s Principle -- Decomposable multiplication
Assumes： Z=y×10111100
Z=y(10000000+111100+100-100)
=y(1×27+1000000-100)
=y(1×27+1×26-22)
=y(1×27+1×26+0×25+0×24+0×23+0×22+0×21+0×20 -1×22 )
= y(1×27+1×26+0×25+0×24+0×23+0×22-1×22 +0×21+0×20)
= y×27+y×1×26+0×25+0×24+0×23 +0×22-y×22 +0×21+0×20)
Only shift
Only shift
add
sub
1 01 111 10 00

## Slide 75: Booth's Algorithm
Idea: If you have a sequence of '1's
  subtract at first '1' in multiplier
  shift for the sequence of '1's
  add where prior step had last '1‘
Result:
  Possibly less additions and more shifts
  Faster, if shifts are faster than additions

## Slide 76: Booth's Algorithm
Example
Logic required identifying the run

## Slide 77: Booth's Algorithm
Analysis of two consecutive bits
Action
  1 0 subtract multiplicand from left
  1 1 no arithmetic operation
  0 1 add multiplicand to left half
  0 0 no arithmetic operation
Bit-1 = '0'
Arithmetic shift right:
  keeps the leftmost bit constant
  no change of sign bit !

## Slide 78: Example with negative numbers
2 * (-3) = - 6
0010 * 1101 = 1111 1010
iteration | step | Multiplicand | product
0 | Initial Values | 0010 | 0000 1101 0
1 | 1.c:10→Prod=Prod-Mcand | 0010 | 1110 1101 0
 | 2: shift right Product | 0010 | 1111 0110 1
2 | 1.b:01→Prod=Prod+Mcand | 0010 | 0001 0110 1
 | 2: shift right Product | 0010 | 0000 1011 0
3 | 1.c:10→Prod=Prod-Mcand | 0010 | 1110 1011 0
 | 2: shift right Product | 0010 | 1111 0101 1
4 | 1.d: 11 → no operation | 0010 | 1111 0101 1
 | 2: shift right Product | 0010 | 1111 1010 1

## Slide 79: 13 * (-11) = - 143 -13= +10011 01101 * 10101 = 11011 10001-->00100 01111
 | step | Multiplicand | product
0 | Initial Values | 01101 | 00000 10101 0
1 | 1.c:10→Prod=Prod-Mcand | 01101 | 10011 10101 0
 | 2: shift right Product | 01101 | 11001 11010 1
2 | 1.b:01→Prod=Prod+Mcand | 01101 | 00110 11010 1
 | 2: shift right Product | 01101 | 00011 01101 0
3 | 1.c:10→Prod=Prod-Mcand | 01101 | 10110 01101 0
 | 2: shift right Product | 01101 | 11011 00110 1
4 | 1.d:01→Prod=Prod+Mcand | 01101 | 01000 00110 1
 | 2: shift right Product | 01101 | 00100 00011 0
 | 1.e:10→Prod=Prod-Mcand | 01101 | 10111 00011 0
 | 2: shift right Product | 01101 | 11011 10001 1

## Slide 80: Faster Multiplication

## Slide 81: END