## Slide 1: Computer Organization & Design —The Hardware/Software Interface
Chapter 4-1 Processor Design

## Slide 2: 重要通知
Mi-term test ： May９
Contents： start to single-cycle CPU design

## Slide 3: Contents
4.1 Introduction
4.2 Logic Design Conventions
4.3 Building a datapath
4.4 A Simple Implementation Scheme
  Single cycle CPU
  Multiple cycle CPU
4.5 An Overview of Pipelining

## Slide 4: 4.1 Introduction
We‘ll look at an implementation of the MIPS
Simplified to contain only:
  memory-reference instructions: lw, sw
  arithmetic-logical instructions: add, sub, and, or, slt
  control flow instructions: beq, j
Generic Implementation:
  use the program counter (PC) to supply instruction address
  get the instruction from memory
  read registers
  use the instruction to decide exactly what to do
What are steps?
How many FUN.?

## Slide 5: An abstract view of the implementation of MIPS

## Slide 6: Contents
4.1 Introduction
4.2 Logic Design Conventions
4.3 Building a datapath
4.4 A Simple Implementation Scheme
4.5 An Overview of Pipelining

## Slide 7: State Elements
Unclocked vs. Clocked
Clocks used in synchronous logic
  when should an element that contains state be updated?
cycle time
rising edge
falling edge

## Slide 8: Our Implementation
An edge triggered methodology
Typical execution:
  read contents of some state elements,
  send values through some combinational logic
  write results to one or more state elements

## Slide 9: Basic elements
Basic logic gate。
  AND：S=A•B
  OR ：S=A+B
  NOT：S=~A
A | B | A•B | A+B | ~A
0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0

## Slide 10: MUX
多路开关：有若干个输入，由控制端决定那一路输入将输出。
  经常是多路并行。
C | S
0 | A
1 | B

## Slide 11: Adder
Half adder：
Full adder：S=A+B
  Input: A, B, C0. Output: Sum, CarryOut
  S = A ⊕ B ⊕ C
  C+1= A•B + B•C + C•A
A | 0 | 0 | 1 | 1
B | 0 | 1 | 0 | 1
S | 0 | 1 | 1 | 0
A | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
B | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
C | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
S | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
C+1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1

## Slide 12: 串行进位加法器
4位串行进位加法器：S=A+B
  各位串行进行。
  同时根据结果产生各种标记状态。
+
Operation
A
S=A+B
32
B
32

## Slide 13: Adder
32-bit Adder
+
Operation
A
S=A+B
32
B
32

## Slide 14: ALU
算术逻辑运算器ALU：即运算器
  5 Operations
  “Set on less than”：
  if A<B then Result=1；
  else Result=0。
Operation | Function
000 | And
001 | Or
010 | Add
110 | Sub
111 | Slt
Less
Binvert
Operation
CarryIn
CarryOut
Result
A
B
00
01
10
11
0
1
3
ALU
Operation
A
Result
32
B
32

## Slide 15: ALU Control
ALUop与Func联合对ALU的控制

## Slide 16: ALU Control
ALU控制：
  ALU由ALUcontrol控制：ALUcontrol由ALUop和指令的低6位(5-0)联合产生ALU控制码。
  这样的好处在于分级控制，对于用的最多的加、减操作，系统只需给出两位的ALUop即可。
Result
Operation
ALUop
ALU
control
Func
[5-0]
32
A
ALU
32
3
2
32
B
zero

## Slide 17: REGISTER
Register
  State element。
  Can be controled by Write signal.
Register
In
Out
Register
In
Out
Write
Read：
Out=Register
Write：
Register=In
Clock cycle

## Slide 18: Memory
存储器：
  可分为指令存储器与数据存储器；
  指令存储器设为只读；输入指令地址，输出指令。
  数据存储器可以读写，由MemRead和MemWrite控制。按地址读出数据输出，或将写数据写入地址所指存储器单元。
Instruction
Instruction
Address
Instruction
memory
MemWrite
Read
data
Address
Data
memory
Write
data
MemRead

## Slide 19: D 触发器
C
D
Q
Q
D
Q
C
Q
Symbol of Latch
C | D | Q(t + 1)
0 | X | hold
1 | 0 | Q=0：reset
1 | 1 | Q=1：set
C | D | S | R | Q(t + 1)
0 | X | X | X | hold
1 | 0 | 0 | 1 | Q=0：reset
1 | 1 | 1 | 0 | Q=1：reset
S
R
Truth table

## Slide 20: Register File
Register File：
  32 32-bit Registers；
  Input: 2 32-bit;
  Output: 32-bit data, 32-bit register number;
  Register write control。

## Slide 21: Register File
Write Register:
  we still use the real clock to determine when to write
Register
C
C
D
D
C
C
D
D
0
1
n-1
n
Register 1
Register n-1
Register n
Register number
Register data
Write
decoder

## Slide 22: Register File

## Slide 23
32×32bits寄存器组硬件描述
Module regs(clk, rst,reg_Rd_addr_A, reg_Rt_addr_B, reg_Wt_addr, wdata, we, rdata_A, rdata_B);
input clk, rst, we;
input [4:0] reg_Rd_addr_A, reg_Rt_addr_B, reg_Wt_addr;
input [31:0] wdata;
output [31:0] rdata_A, rdata_B;
reg [31:0] register [1:31]; // r1 - r31
integer i;
assign rdata_A = (reg_Rd_addr_A == 0)? 0 : register[reg_Rd_addr_A]; // read
assign rdata_B = (reg_Rt_addr_B == 0)? 0 : register[reg_Rt_addr_B]; // read
always @(posedge clk or posedge rst)
begin
if (rst==1) begin // reset
for (i=1; i<32; i=i+1)
register[i] <= 0;
end
else begin
if ((reg_Wt_addr != 0) && (we == 1)) // write
register[reg_Wt_addr] <= wdata;
end
end
endmodule

## Slide 24: 32个Register的功用
寄存器组有32个32位寄存器，其功用分配如下表：

## Slide 25: The other elements
Sign Extend：
  将16位的补码表示的有符号立即数，扩展为32位。
  方法：只需重复符号位即可。
Shift：
  Shift 2 bits left。
  方法：将输入高移2位接输出，输出的低两位接0。
16
32
Sign
extend
D15
D14
.
.
.
D00
D31
.
.
.
D16
D15
D14
.
.
.
D00
Shift
left 2
D31
D30
D29
.
.
.
.
.
.
D02
D01
D00
D31
D30
D29
.
.
.
.
.
.
D02
D01
D00

## Slide 26: Simple Implementation
Include the functional units we need for each instruction
Why do we need this stuff?
A
L
U
c
o
n
t
r
o
l
R
e
g
W
r
i
t
e
R
e
g
i
s
t
e
r
s
W
r
i
t
e
r
e
g
i
s
t
e
r
R
e
a
d
d
a
t
a
1
R
e
a
d
d
a
t
a
2
R
e
a
d
r
e
g
i
s
t
e
r
1
R
e
a
d
r
e
g
i
s
t
e
r
2
W
r
i
t
e
d
a
t
a
A
L
U
r
e
s
u
l
t
A
L
U
D
a
t
a
D
a
t
a
R
e
g
i
s
t
e
r
n
u
m
b
e
r
s
a
.
R
e
g
i
s
t
e
r
s
b
.
A
L
U
Z
e
r
o
5
5
5
3

## Slide 27: Instruction types
Opcode rs rt rd shamt function
R type
Opcode rs rt immediate
I type
Opcode Address
J type

## Slide 28: Contents
4.1 Introduction
4.2 Logic Design Conventions
4.3 Building a datapath
4.4 A Simple Implementation Scheme
4.5 An Overview of Pipelining

## Slide 29: Instruction fetching three elements
PC
I
n
s
t
r
u
c
t
i
o
n
m
e
m
o
r
y
R
e
a
d
a
d
d
r
e
s
s
I
n
s
t
r
u
c
t
i
o
n
Add Sum
Instruction memory
Program counter
Adder

## Slide 30: Instruction fetching unit
P
C
I
n
s
t
r
u
c
t
i
o
n
m
e
m
o
r
y
R
e
a
d
a
d
d
r
e
s
s
I
n
s
t
r
u
c
t
i
o
n
4
A
d
d
CPU

## Slide 31: More Implementation Details
Abstract / Simplified View:

## Slide 32: R type Instruction & Data stream
op(6)
rs(5)
rt(5)
rd(5)
shamt
func(6)
rs
rt
rd
bit21-25
bit16-20
bit11-15
Bnegate | op | function
0 | 00 | and
0 | 01 | Or
0 | 10 | Add
1 | 10 | Sub
1 | 11 | Slt
Registers
Read reg. address1
Read reg. address2
Write reg. address
Write data
Read data1
Read data2
ALU result
Zero
ALU
3
RegWrite
ALU operation
control
32bits data

## Slide 33: I type Instruction & Data stream
rs
rt
rt
Registers
Read reg. address1
Read reg. address2
Write reg. address
Write data
Read data1
Read data2
ALU result
Zero
ALU
3
RegWrite
ALU operation
control
address
Write data
Read data
Sign extend
op(6)
rs(5)
rt(5)
Immediate data
bit0-15
bit21-25
bit16-20
MenWrite
MenRead
16
32
32bits data
lw $t0, 200($s2)
if $s2=1000，it will load word in element number 1200 to $t0
Sw $t0, 200($s2)
Data
Memory

## Slide 34: I type Instruction & Data stream of beq
rs
rt
rt
Registers
Read reg. address1
Read reg. address2
Write reg. address
Write data
Read data1
Read data2
ALU result
Zero
ALU
3
RegWrite
ALU operation
Sign extend
op(6)
rs(5)
rt(5)
offset
bit0-15
bit21-25
bit16-20
16
32
Shift
left 2
PC+4 from instructiondatapath
ADD
To PC

## Slide 35: combine the implementation R-type and I type

## Slide 36: Contents
4.1 Introduction
4.2 Logic Design Conventions
4.3 Building a datapath
4.4 A Simple Implementation Scheme
4.5 An Overview of Pipelining

## Slide 37: Building the Datapath
Use multiplexors to stitch them together
Note : control signals Page 306 F4.15
0
1
0
1
0
1

## Slide 38: Control
Analyse for cause and effect
Information comes from the 32 bits of the instruction
Selecting the operations to perform (ALU, read/write, etc.)
Controlling the flow of data (multiplexor inputs)
ALU's operation based on instruction type and function code

## Slide 39: Instruction Code
jal ?????? Address r31PC+4
lui ?????? 00000 rt immediate
shift 000000 00000 rt rd shamt ??????

## Slide 40: What should ALU do ?
e.g. what should the ALU do with these instructions
Example: lw $1, 100($2) OP rs rt 16 bit displacement
ALU control input
3 -types
Why is the code for subtract 110 and not 011?
(100011)35
2
1
100
B negate | op | function
0 | 00 | and
0 | 01 | Or
0 | 10 | Add
1 | 10 | Sub
1 | 11 | Slt
(101011)43
2
1
100
000000(00)
rs(5)
rt(5)
rd(5)
shamt
func(6)
lw
sw
R
00
01
10
ALU op

## Slide 41: Scheme of Controller
2-level decoder
First
Main
decoder
ALU
Decoder
Second
Signals for Other
Components (7)
op(6)
rs(5)
rt(5)
rd(5)
shamt
func(6)
ALU operation(3)
ALU op(2)
instruction op code
(6)

## Slide 42: The ALU control is where and other signals(7)
1
0
0
1
0
1

## Slide 43: signals for datapath Defined 7+2 control (p. 307) f4.16
Signal name | Effect when deasserted(=0) | Effect when asserted(=1)
RegDst | Select register destination number from the rt(20:16) when WR | Select register destination number from the rd(15:11) when WB
RegWrite | None | Register destination input is written with the value on the Write data input
ALUScr | The second ALU operand come from the second register file output (Read data 2) | The second ALU operand is the sign-extended lower 16 bits of the instruction..
PCSrc | The PC is replaced by the output of the adder that computers the value PC+4 | The PC is replaced by the output of the adder that computers the branch target.
MemRead | None | Data memory contents designated by the address input are put on the Read data output.
MemWrite | None | Data memory contents designated by the address input are replaced by value on the Write data input.
MemtoReg | The value fed to register Write data input comes from the Alu | The value fed to the register Write data input comes from the data memory.

## Slide 44: Designing the ALU decoder (Second level)
Must describe hardware to compute 3-bit ALU conrol input
Instruction opcode | ALUOp | Instruction operation | Funct field | Desired ALU action | ALU control Input
LW | 00 | Load word | xxxxxx | Load word | 0010
SW | 00 | Store word | xxxxxx | Store word | 0010
Beq | 01 | branch equal | xxxxxx | branch equal | 0110
R-type | 10 | add | 100000 | add | 0010
R-type | 10 | subtract | 100010 | subtract | 0110
R-type | 10 | AND | 100100 | AND | 0000
R-type | 10 | OR | 100101 | OR | 0001
R-type | 10 | Set on less than | 101010 | Set on less than | 0111

## Slide 45: Truth Table for ALU decoder
Describe it using a truth table (can turn into gates):
don’t care

## Slide 46: **The ALU control signals---logic circuit
0 | x | x | 1
0 | 0 | x | x
x | x | x | x
x | x | x | 1
F1F0
F3F2
F1
1 | x | x | 1
0 | 0 | x | X
x | x | x | X
1 | x | x | 1
F1F0
F3F2
F2
0 | x | x | 0
0 | 1 | x | X
x | x | x | X
x | x | x | 1
F1F0
F3F2
F0
F3

## Slide 47: Designing the Main Control Unit (First level)
Main Control Unit function
  ALU op (2)
  Divided 7 control signals into 2 groups
    4 Mux
    3 R/W
ALU
control
Instruction op code (6)
ALU op (2)
Mux (4)
R/W (3)

## Slide 48
Truth Table for Main decoder

## Slide 49: Circuitry of main Controller
Simple combinational logic (truth tables)
opcode | output | 
000000 | R-format | 
100011 | lw | 
101011 | sw | 
000100 | beq | 
L/S 00
beq 01
R-type 10

## Slide 50: Controller Implementation
And
SrcB=
MRead=LW+LH+LB
MWrite=SW+SH+SB
M2Reg=LW+LH+LB
RegDes=ALURI+LW+LUI (rt)
Wreg=ALURR+ALURI+Load
+JAL+LUI+shift
=~(Branch + J + JR + Store)
Taken=Beq*Zero + Bne*~Zero
SrcA=SLL + SRL = shift
…
ALUop
opcode6
Func6
Or
ALU-R-R
ALU-R-I
LW
SW
BEQ
BNE
J
JAL
JR
LUI
SHIFT
controller
Zero
ALURI+LW+SW+SHIFT

## Slide 51: Our Simple Control Structure
All of the logic is combinational
We wait for everything to settle down, and the right thing to be done
  ALU might not produce right answer? right away
  we use write signals along with clock to determine when to write
Cycle time determined by length of the longest path
We are ignoring some details like setup and hold times
Instruction n
Instruction n+1

## Slide 52: The simple Datapath with the control unit
Read
address
Instruction
[31-0]
Instruction
memory
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 1
Read
data 2
Registers
Address
Data
memory
Read
data
Write
data
0
M
U
X
1
0
M
U
X
1
1
M
U
X
0
0
M
U
X
1
ALU
ALU
result
Zero
Add
ALU
result
ALU
control
Control
Add
pc
4
Sign
extend
Instruction [31-26]
Instruction [25-21]
Instruction [20-16]
Instruction [15-11]
Instruction [15-0]
16
32
RegDst
Branch
MemRead
MemtoRead
ALUOp
MemWrite
ALUSrc
RegWrite
Instruction [5-0]
R-type |  |  |  |  | 
Op | rs | rt | rd | shamt | Funct
I-type |  |  | 
Op | rs | rt | Immediate
Jump-type | 
Op | address
Shift
left 2
Shift
left 2
26
Instruction [25-0]
1
M
U
X
0
jump
jump address[31-0]
28
PC+4[31-28]

## Slide 53: The Datapath in operation for R-type
Address
Data
memory
Read
data
Write
data
Add
ALU
result
Shift
left 2
Shift
left 2
26
Instruction [25-0]
jump address[31-0]
28
PC+4[31-28]
Sign
extend
Instruction [15-0]
16
32
I-type |  |  | 
Op | rs | rt | Immediate
Jump-type | 
Op | address
Read
address
Instruction
[31-0]
Instruction
memory
Read
register 1
Read
register 2
Write
register
Write
data
Read
data 1
Read
data 2
Registers
0
M
U
X
1
0
M
U
X
1
1
M
U
X
0
0
M
U
X
1
ALU
ALU
result
Zero
ALU
control
Control
Add
pc
4
Instruction [31-26]
Instruction [25-21]
Instruction [20-16]
Instruction [15-11]
RegDst
Branch
MemRead
MemtoRead
ALUOp
MemWrite
ALUSrc
RegWrite
Instruction [5-0]
R-type |  |  |  |  | 
Op | rs | rt | rd | shamt | Funct
1
M
U
X
0
jump
add sub and or slt

## Slide 54: The Datapath in operation for load
26
28
Instruction [15-11]
Write
data
Add
ALU
result
Shift
left 2
Read
register 2
Read
data 2
Instruction [20-16]
Instruction [5-0]
Shift
left 2
Instruction [25-0]
jump address[31-0]
PC+4[31-28]
R-type |  |  |  |  | 
Op | rs | rt | rd | shamt | Funct
Jump-type | 
Op | address
Read
address
Instruction
[31-0]
Instruction
memory
Read
register 1
Write
register
Write
data
Read
data 1
Registers
Address
Data
memory
Read
data
0
M
U
X
1
0
M
U
X
1
1
M
U
X
0
0
M
U
X
1
ALU
ALU
result
Zero
ALU
control
Control
Add
pc
4
Sign
extend
Instruction [31-26]
Instruction [25-21]
Instruction [15-0]
16
32
RegDst
Branch
MemRead
MemtoRead
ALUOp
MemWrite
ALUSrc
RegWrite
I-type |  |  | 
Op | rs | rt | Immediate
1
M
U
X
0
jump
load instruction

## Slide 55: The Datapath in operation for SW
Read
data
1
M
U
X
0
Write
register
Write
data
0
M
U
X
1
26
28
Instruction [15-11]
Add
ALU
result
Shift
left 2
Read
data 2
Instruction [5-0]
Shift
left 2
Instruction [25-0]
jump address[31-0]
PC+4[31-28]
R-type |  |  |  |  | 
Op | rs | rt | rd | shamt | Funct
Jump-type | 
Op | address
Read
address
Instruction
[31-0]
Read
register 1
Read
data 1
Registers
Data
memory
0
M
U
X
1
Control
Add
pc
4
Sign
extend
Instruction [31-26]
Instruction [25-21]
Instruction [15-0]
16
32
RegDst
Branch
MemRead
MemtoRead
ALUOp
MemWrite
ALUSrc
RegWrite
I-type |  |  | 
Op | rs | rt | Immediate
1
M
U
X
0
jump
store instruction
Read
register 2
Instruction [20-16]
Instruction
memory
Write
data
Address
0
M
U
X
1
ALU
ALU
result
Zero
ALU
control

## Slide 56: The Datapath in operation for BEQ
Write
data
Address
ALU
result
Read
data
1
M
U
X
0
Write
register
Write
data
0
M
U
X
1
26
28
Instruction [15-11]
Instruction [5-0]
Shift
left 2
Instruction [25-0]
jump address[31-0]
PC+4[31-28]
R-type |  |  |  |  | 
Op | rs | rt | rd | shamt | Funct
Jump-type | 
Op | address
Read
address
Instruction
[31-0]
Read
register 1
Read
data 1
Registers
Control
Add
pc
4
Sign
extend
Instruction [31-26]
Instruction [25-21]
Instruction [15-0]
16
32
RegDst
Branch
MemRead
MemtoRead
ALUOp
MemWrite
ALUSrc
RegWrite
I-type |  |  | 
Op | rs | rt | Immediate
1
M
U
X
0
jump
beq instruction
Read
register 2
Instruction [20-16]
Instruction
memory
0
M
U
X
1
ALU
ALU
control
Add
ALU
result
Shift
left 2
0
M
U
X
1
Data
memory
Read
data 2
Zero

## Slide 57: j instruction
instruction format
  j Label
Implementation
  pc = pc28~31 ## 26bits-address × 4
(000010)2
26 bits address

## Slide 58: The Datapath in operation for j
Registers
0
M
U
X
1
ALU
control
0
M
U
X
1
Read
data 2
Zero
Read
register 1
Read
data 1
Read
register 2
Add
ALU
result
Data
memory
Sign
extend
Instruction [25-21]
Instruction [15-0]
16
32
Instruction [20-16]
ALU
Shift
left 2
I-type |  |  | 
Op | rs | rt | Immediate
Write
data
Address
ALU
result
Read
data
0
M
U
X
1
Write
register
Write
data
0
M
U
X
1
Instruction [15-11]
Instruction [5-0]
R-type |  |  |  |  | 
Op | rs | rt | rd | shamt | Funct
Control
RegDst
Branch
MemRead
MemtoRead
ALUOp
MemWrite
ALUSrc
RegWrite
1
M
U
X
0
jump
jump instruction
Instruction
memory
Jump-type | 
Op | address
28
Shift
left 2
Instruction [25-0]
jump address[31-0]
PC+4[31-28]
Instruction [31-26]
26
Read
address
Instruction
[31-0]
Add
pc
4

## Slide 59: Single Cycle Implementation performance for lw
Calculate cycle time assuming negligible delays except:
  memory (2ns), ALU and adders (2ns), register file access (1ns)
2ns
2ns
2ns
1+1=ns

## Slide 60: The time sequence in single-cycle implementation
PC

## Slide 61: ISE Block RAM design
http://wenku.baidu.com/view/5231ba778e9951e79b892746.html

## Slide 62: **Performance in Single Cycle Implementation
Let’s see the following table:
Instruction class | Instruction memory | Register read | ALU | Data memory | Register write | Total
R-format | 2 | 1 | 2 |  | 1 | 6 ns
Load word | 2 | 1 | 2 | 2 | 1 | 8 ns
Store word | 2 | 1 | 2 | 2 |  | 7 ns
Branch | 2 | 1 | 2 |  |  | 5 ns
Jump | 2 |  |  |  |  | 2 ns
The conclusion:
  Different instructions needs different time.
  The clock cycle must meet the need of the slowest instruction. So, some time will be wasted.

## Slide 63: The CPU Performance Equation
CPU time=IC* CPI* CC

## Slide 65
CPU performance is dependent upon three characteristics:
  clock cycle ( CC )
  clock cycles per instruction ( CPI )
  and instruction count (IC ).
It is difficult to change one parameter in complete isolation from others because the basic technologies involved in changing each characteristic are interdependent:
  Clock cycle time—Hardware technology and organization
  Clock cycle time—Hardware technology and organization
  Instruction count—Instruction set architecture and compiler technology

## Slide 66: MIPS (million instruction per second)
Three problems with MIPS:
  MIPS is dependent on the instruction set, making it difficult to compare MIPS of computers with different instruction sets.
  MIPS varies between programs on the same computer.
  Most importantly, MIPS can vary inversely to performance!
The bigger the MIPS, the faster the machine.

## Slide 67: Single Cycle Problems
what if we had a more complicated instruction like floating point?
  If so, the waste of time will be much more large.
wasteful of area. The reason is the following:
  Let’s see the instruction ‘mult’. This instruction needs to use the ALU repeatedly. But, in the single cycle implementation, one ALU can be used only once in one clock cycle. So,the instruction ‘mult’ will need many ALUs. The CPU will be very large.

## Slide 68: One Solution for Single Cycle Problems
One Solution:
  Use a smaller cycle time
  Let different instructions take different numbers of cycles
a Multicycle datapath:

## Slide 69: contents
4.1 Introduction
4.2 Logic Design Conventions
4.3 Building a datapath
4.4 A Simple Implementation Scheme
4.5 A Multicycle Implementation
4.5 Microprogramming
4.6 Exception

## Slide 70: END